## Slide 1: Innovative Ideas in Lunar Calibration for IR
Dr. Martin Burgdorf
20.03.2025
Foto: UHH/CLICCS

## Slide 2: Agenda
Introduction
Radiometric reference: CrIS on Suomi
Example: Calibration Check of HIRS
Spatially Resolved Observations of the Moon
Future Projects
Summary and Discussion

## Slide 3: Introduction
1
Foto: UHH/CLICCS

## Slide 4: Establish the Moon as Radiometric Reference in IR
Cal. Landsat with Moon suggested `85
Probl. With mid-IR: large contrast
Solution: Disk-averaged irradiance
One reference:
CrIS
Main aim: check radiometric stability

## Slide 5: Radiometric Reference
2
Foto: UHH/CLICCS

## Slide 6: Reference: CrIS on Suomi
Yong Chen: 667 + 326 files with lunar spectra, , phase…
Oliver Lemke: Table with TB and 11 observer quantities
For given wavelength (range) 0:
fit([phase, distM-S], TB, poly12)
Empirical irradiance model at 0 with 5 coefficients (18 in VIS/NIR)

## Slide 7: Example: Comparison to CrIS on NOAA-20
Moon observed between First Quarter and Waxing Gibbous
Compare to Suomi @ same
Removed 9 obvious outliers
TB (obs. With SNPP) – TB (obs. With N20) = 0.420.02 K
Absolute accuracy 0.2 K

## Slide 8: Check the Calibration of HIRS
3
Foto: UHH/CLICCS

## Slide 9: Example: Check Radiometric Calibration of HIRS/4
Moon observed with HIRS since end of seventies
HIRS/4 FoV = 2x Moon (area)
Method in C. Seibert‘s master thesis
Dataset at
https://zenodo.org/records/6865664

## Slide 10: Do Measurements of CrIS and HIRS/4 Match Well?
8 obs., 45 < phase < 90
Average of 4 channels
HIRS – CrIS = 0.71.2 K
1 K in TB is 3% in radiance
See Fig. 8 in Müller et al 2021
See Fig. 6 in Kieffer 2022

## Slide 11: Spatially Resolved Observations of the Moon
4
Foto: UHH/CLICCS

## Slide 12: Central Pixel on Venusian Disk - an Alternative
Diameter of Venus up to 1 arcmin
TB stable for several Earth days
Best suited for > 8 m
Problem: archived files have calibration applied only to pixels pointing at Earth
https://ieeexplore.ieee.org/abstract/document/10641924

## Slide 13: Future Projects: Far IR
5
Foto: UHH/CLICCS

## Slide 14: Radiance of the Moon According to Model by Thomas Müller (MPE)
One complete lunation covered
is phase angle
Validate model with infrared and microwave sounder
Spectral features of Ilmenite or fool‘s gold at 300 – 600 cm-1?

## Slide 15: Summary
6
Foto: UHH/CLICCS

## Slide 16: Radiometric Calibration Check in one Day (LEO)
ID Moon in DSV – cal. rejects or manoeuvres
Calculate radiance for max. signal
Compare to CrIS:
(3.9 – 15.4 m), date/time (phase), s.s.p.
No need for SNOs, check abs. cal., stability, non-lin., pointing, diameter of FOV,…
Blackbody still needed?

## Slide 17: Open Questions and Discussion
Radiance from reference can be calculated with existing programs
Should radiance from Moon be available by GSICS?
Put TB = f(phase, distM-S) for three and data files / programs in repository?

## Slide 18: Contact
Martin Burgdorf Research Scientist
Centrum für Erdsystemforschung und Nachhaltigkeit (CEN)
Universität Hamburg Bundesstraße 53 20146 Hamburg
+49 40 42838-8121 martin.burgdorf@uni-hamburg.de