## Slide 1: GSICS Agency Report 2025
Lei DING
Contributor: Shijie XIN, Yang WANG, Chunyuan SHAO, etc.
Shanghai Institute of Technical Physics, CAS
（SITP）

## Slide 2: Presentation Overview
Summary of Agency’s GSICS Activities, Actions, and Achievements
Agency’s Support to EP Activities
Agency’s Support to GDWG Activities
Agency’s Support to GRWG Activities
Agency’s Instruments Updates & Planned launches that are relevant to GSICS (stress new programs and significant accomplishments)
Agency’s Calibration Major Updates

## Slide 3: Activities and Achievements
Reprocessing FY-3G HAOC calibration data
Inter-Sensor Comparison using HAOC data
Pre-launch calibration for FY-3H MERSI, FY-3H HIRAS, FY-3H GAS, DQ-2/HIACS
Developing Infrared Benchmark instrument

## Slide 4: Participation in EP, GDWG, GRWG
Points of contacts/meeting participants:
  EP: Lei Ding
  GDWG:
  GRWG:
Main contribution to GDWG actions
  …
Main contribution to GRWG actions
  Calibration for instrumens, FY-3H, FY-4C, DQ-2
Comments, feedback
  …..

## Slide 5: Summary of SITP’s GSICS Activities
Payloads under construction
  Enhanced AGRI, GIIRS onboard FY-4C, planned to be launched in 2025.
  MERSI-III, HIRAS-II, GAS-2(Greenhouse-Gas Absorption Spectrometer) onboard FY-3H , planned to be launched in 2025
  Enhanced AGRI, GIIRS onboard FY-4D, scheduled to be launched in 2026.
  MERSI-LL, HIRAS-II onboard FengYun 3J, scheduled to be launched in 2026.
  Enhanced AGRI, GIIRS onboard FY-4E, scheduled to be launched in 2027.
  MERSI-RM, HAOC(High Accuracy On-board Calibrator) onboard FY-3I (Rainfall) mission, scheduled to be launched in 2027;
  Infrared Benchmark Payload, scheduled to be launched around 2027;

## Slide 6: Summary of SITP’s GSICS Activities
Operational service
  AGRI, GIIRS,GHI onboard FengYun 4B, launched in June 2021.
  MERSI-LL, HIRAS-II onboard FengYun 3E, launched in July 2021.
  AHSI (Advanced Hyperspectral Imager) onboard GaoFen 5-02, launched in Sept. 2021.
  Thermal Infrared sensor onboard SDGSAT-1(CASEarth), launched in Nov. 2021.
  AHSI onboard ZY-1 02E (Ziyuan-1 02E) launched in Dec. 2021;
  WSI(Wide-field-of-view Spectral Imager) onboard DaQi-1 launched in April 2022;
  AHSI (Advanced Hyperspectral Imager) onboard GF-5 01A mission, launched in Dec. 2022;
  MERSI-RM, HAOC(High Accuracy On-board Calibrator), PMAI onboard FY-3G(Rainfall) mission, launched in April 2023;
  MERSI-III, HIRAS-II, ERM onboard FY-3F(AM), launched in July 2023;
  PMRIS(Programmable Medium Resolution Imaging Spectrometer) onboard HY-3A(HaiYang 3A) mission, launched in Noverber 2023;

## Slide 7: HIRAS-II onboard FY-3
Band | Spectral Range (cm-1) | Spectral Resolution (cm-1) | Sensitivity NET@280K | Radiometric accuracy | Spectral accuracy
LW | 650～1136 （15.38m～8.8 m） | 0.625 | 0.2～0.8K | 0.4～1K | 7ppm/ 5ppm
MW1 | 1210～1750 （8.26m～5.71 m） | 1.25(0.625) | 0.2～0.3K | 0.4～0.5K | 
MW2 | 2155～2550 （4.64m～3.92 m） | 2.5(0.625) | 0.3～0.5K | 0.5～0.6K | 
Parameters | Specification
Scan Period | 8s
FOV size | 1
Pixels per scan line | 252 (9 FOVs x 28 FORs)
Maximum scan angle |  48.6
Nadir spatial resolution | 14km
detectors define | 3*3
Direction pointing bias | ＜0.06°
Compared with the FY-3D/HIRAS HIRAS-II focuses on improving the detection sensitivity, spectral and radiative accuracy.
The observation time of each scan line of HIRAS-II is changed from 10 to 8 seconds, the view angle is changed from 1.1 to 1 degree and the nadir spatial resolution improved from 16 to 14 km.
In addition, the detector array is changed from 2×2 to 3×3.
The observed spectra of the instrument are divided into three infrared bands: long wave (LW), medium wave 1 (MW1) and medium wave 2(MW2).
The maximum optical path difference of the interferometer is 0.8cm, which will produce a basic resolution of 0.625cm-1.

## Slide 8: Calibration of HIRAS-II
FY-3H/HIRAS-II Spectral calibration
FOV | FOV1 | FOV2 | FOV3 | FOV4 | FOV5 | FOV6 | FOV7 | FOV8 | FOV9
LW pre-launch/ppm | 0.84 | -3.58 | 1.26 | -2.63 | 0.84 | 1.05 | 2.42 | 0.21 | 2.63
MW1 pre-launch/ppm | 1.85 | 1.31 | -0.85 | 3.17 | 0.93 | 3.01 | -1.00 | 3.17 | -2.86
MW2 pre-launch/ppm | 2.97 | -3.34 | -1.10 | 2.42 | -2.42 | -0.18 | 3.93 | 3.84 | -0.73
Spectral calibration biases are within 4 ppm after off-axis parameters adjustment in LW, MW1 and MW2 bands.
FOV | FOV1 | FOV2 | FOV3 | FOV4 | FOV5 | FOV6 | FOV7 | FOV8 | FOV9
LW pre-launch/ppm | -0.84 | -2.73 | 1.684 | -1.68 | 0.421 | 0.842 | 0.526 | -1.89 | 1.68
MW1 pre-launch/ppm | 0.15 | 0.07 | 2.62 | -2.47 | -0.30 | -0.30 | -0.23 | 0.38 | 0.07
MW2 pre-launch/ppm | -0.86 | -1.73 | -0.22 | 1.14 | -0.77 | 0.59 | -1.73 | 1.60 | 0.32
DQ-2/HIACS Spectral calibration
Spectral calibration biases are within 3 ppm after off-axis parameters adjustment in LW, MW and SW bands.

## Slide 9: Calibration of HIRAS-II
FY-3H/HIRAS-II Radiometric calibration
LW and MW1 exhibit obvious Non-Linearity characteristics.
• After NL correction, LW and MW1 channels calibration biases are within 0.5 K.
• MW2 without NL correction, but displays abnormal large bias structure due to weak sigal and large noise for low temperature
Before Non-Linearity Correction
After Non-Linearity Correction
pre-launch test

## Slide 10
DQ-2/HIACS Radiometric calibration
LW exhibit obvious Non-Linearity characteristics.
After NL correction, LW MW and SW channels calibration biases are within 0.2~0.5 K.
Before Non-Linearity Correction
After Non-Linearity Correction
pre-launch test

## Slide 11: Infrared Benchmark Payload
Uncertainty evaluation of space infrared radiation benchmark payload
Uncertainty System Analysis
The uncertainty ua2 of the nonlinearity of the system response is recorded as the uncertainty of the nonlinear contribution a2.
The combined uncertainty of the DC quantities VECT,VICT,VST is uv.
The combined uncertainty of the radiation spectra CECT,CICT,CST is uC.
There are uncertainties uεICT, uεST , uTICT, uTST of the high-temperature & the low-temperature calibration radiation source.
Temperature changes of the temperature field inside the instrument will also introduce uncertainty uTR.
Progress & Achievements
Type | Items | Uncertainty Sources
Radiometric Calibration Uncertainty | u(TR,ICT) | System temperature stability and non-uniformity
 | u(TR,ST) | 
 | u(a2) | FTS uncertainty relation
 | u(CICT) | Interferometric efficiency uncertainty, detector temperature stability, measured complex spectral noise
 | u(CECT) | 
 | u(CST) | 
 | u(VICT) | 
 | u(VECT) | 
 | u(VST) | 
 | SCR*RECT | Stray light
Uncertainty of infrared radiation reference source | Temperature u1 | Thermometer calibration, phase change reproducibility, temperature control stability, temperature uniformity, measurement noise
 | Emissivity u2 | Blackbody temperature, heated halo temperature & emissivity, ambient temperature, radiation measurement noise, radiation angle coefficient
 | Ambient temperature u3 | measurement noise

## Slide 12: Infrared Benchmark Payload
Gallium fixed point BB
Variable temperature BB(with 3 micro phase change fixed point)
Low temperature BB(with 3 micro phase change fixed point)
Overview of infrared radiation reference SI-traceable subsystem
Low temperature BB
Temperature range：220K~330K
Caliber：130mm
Emissivity：0.999
Temperature uniformity @bottom：20mK
Reproducibility of phase transition temperature ：20mK
Variable temperature BB
Temperature range：220K~330K
Caliber：130mm
Emissivity：0.999
Temperature uniformity @bottom：20mK
Reproducibility of phase transition temperature ：20mK
Gallium fixed point BB
Temperature range ：270K~320K
Caliber ：130mm
Emissivity ：0.999
Reproducibility of phase transition temperature ：20 mK
Scanning mirror
Heated Halo

## Slide 13: Infrared Benchmark Payload
Uncertainty of Prototype
0.085K（k=1）
Designed for GSICS Inter-Calibration Products
Notes: 根据红外辐射基准载荷辐射测量合成标准不确定度公式，可以得到载荷的各谱段不确定度结果，如图所示

## Slide 14
THANK YOU!
Welcome to SITP

## Slide 15: Thank you!