## Slide 1
Update on LSICS Development
By the LSICS Development Team:
  Tom Stone, USGS
  Sebastien Wagner, EUMETSAT
  Hugh Kieffer, Celestial Reasonings
  Matthijs Krijger, Earth Space Solutions
  Fangfang Yu, NOAA
  Bikash Basnet, NOAA
  Masaya Takahashi, JMA
  Fred Wu, NOAA — support and technical review
With technical expertise provided by:
  Vincent Debaecker, Telespazio
  Romain Degoul, Telespazio
  (by contract with EUMETSAT)

## Slide 2: Introduction
LSICS: Lunar Spectral Irradiance Calibration System
  The new GSICS reference for lunar calibration
  proposed at the GSICS 2023 annual meeting
  development support provided by NOAA
  the LSICS concept was endorsed by the GSICS EP at the 2024 meeting
Objective: replacement for the GIRO (GSICS Implementation of ROLO model)
  GIRO has been in use since 2014
    known limitations of the ROLO model (e.g. absolute bias)
    requires usage agreement
  desire to use a modern programming language — python was chosen
  desire to apply newly-developed lunar model(s)
Requirement: back-compatibility with GIRO I/O and SRF files

## Slide 3: LSICS Design Characteristics
Modular code structure (flowchart next slide)
  Ingest and Geometry, Disk Reflectance, Spectral Irradiance modules
  intermediate files used for I/O by the modules
    for record-keeping
    to enable running the modules independently
Required feature: interchangeable central Disk Reflectance module
  to allow implementing different lunar models within the existing structure
  enabled by standard interfaces with the other modules
    Interface Control Document (ICD) currently under development
Process logging at runtime
  detailed output written to log files
  progress diagnostics printed to screen

## Slide 4
Ingest and Geometry Calculation Module
Operation: compute Lunar Observation Angle Set (LOAS)
• Phase angle (signed)
• Sub-solar longitude and latitude
• Sub-observer longitude and latitude
Intermediate Data Files
• Geometry: LOAS
• Spectral: SRF, std units
Lunar Disk Reflectance Module
Operation: compute lunar disk equivalent reflectance spectra
• set up basis functions
• reconstruct disk reflectance model
• compute model on operating wave- length set using LOAS parameters
Spectral Irradiance Module
Operation: produce model irradiances in sensor bands
• Convolve disk reflectance, solar irradiance and SRF
• Apply distance corrections
Model Definitions
• Operating wavelength set
• Basis function coefficients
Reference Spectra
• Lunar reflectance
• Solar Irradiance
Intermediate Data Files
• Operating wavelengths
• Disk reflectance spectra
Input Files
• Observation times
• Observer locations
• Sensor SRFs
Final Outputs
• Lunar spectral irradiances for input observations in sensor spectral bands
Framework flowchart presented to the GSICS 2023 Annual meeting

## Slide 5: LSICS Design Characteristics
Modular code structure (flowchart next slide)
  Ingest and Geometry, Disk Reflectance, Spectral Irradiance modules
  intermediate files used for I/O by the modules
    for record-keeping
    to enable running the modules independently
Required feature: interchangeable central Disk Reflectance module
  to allow implementing different lunar models within the existing structure
  enabled by standard interfaces with the other modules
    Interface Control Document (ICD) currently under development
Process logging at runtime
  detailed output written to log files
  progress diagnostics printed to screen

## Slide 6: Distribution and Usage
Public access for users (upon formal release): downloadable python notebook
  GitLab repository, hosted at EUMETSAT
Creative Commons license
  CC BY–ND — attribution required, no code derivatives allowed
  avoids having a formal usage agreement
Digital markers and public signature key
  to ensure that output products have been generated by the official agreed version of LSICS
  implemented using JSON tokens

## Slide 7: Current Status
end-to-end code is written; a preliminary version has been operated
  some desired capabilities are still to be implemented, e.g. full GIRO compatibility
  the initial Disk Reflectance module runs H. Kieffer’s SLIMM model
established file formats, contents and filename conventions
  netCDF is adopted for I/O, SRF, and intermediate files
  naming conventions for I/O and SRF files follow WMO guidelines
testing the Ingest and Geometry module has been completed and validated
  SPICE tools used for ephemeris and photometric geometry calculations
end-to-end operation has been demonstrated for one test case (GOES-16)
  outputs have been validated against the original SLIMM system
TSIS-1 HSRS is implemented for reflectance-to-irradiance conversions
  GSICS-recommended solar spectrum
digital markers implemented, check that outputs generated by unaltered code

## Slide 8: Next Steps
special handling for GIRO inputs
  concatenating multiple single-observation files into a multiple-observation sequence
  requires generating a new filename to indicate the observation time range
defining and creating a benchmark for testing
  validation against the original lunar model implemented in the DR module
  new enhancements implemented in LSICS
  new lunar models
formal documentation
  functional requirements, code structure, file and data formats (I/O, SRF and internal/intermediate files), module interfaces (Interface Control Document)
  lunar model functional description
implementing a different lunar model — coding a compatible DR module
  motivation for ICD development
release of version 1.0