## Slide 1
Improved Deep Convective Cloud Characterization Designed to Monitor the VIIRS Reflective Solar Band Stability
Prathana Khakurela, David Doellingb, Conor Haneya, Rajendra Bhattb, Arun Gopalana, Benjamin Scarinob
AMS 2025 annual meeting, Jan 16, 2025,
New Orleans, LA
aAnalytical Mechanics Associates
bNASA Langley Research Center

## Slide 2
Background
NASA’s CERES Project, provides long-term global 1° gridded regional broadband fluxes to monitor the Earth’s climate.
  CERES instruments are onboard Terra, Aqua, SNPP, and NOAA-20 satellites
  Radiances are converted to fluxes using scene specific angular directional models, requiring stable MODIS and VIIRS analogous radiances for consistent cloud properties.
  The CERES Imager and Geostationary Calibration Group ensures accurate calibration for cloud and flux measurements
Deep convective clouds (DCCs) serve as the brightest tropical Earth invariant targets (IT) located at the top of the atmosphere to monitor imager calibration stability.
  DCC-IT approach, introduced by Hu et al. (2004), monitored the stability of the CERES SW radiance using the PDF mode statistics after applying the Hu BRDF, based on the CERES instrument Rotating Azimuth Plane Mode Scan radiances
  Hu BRDF model is suited for visible channels
  SWIR channel specific Empirical BRDF monthly models is best suited for capturing the seasonal variability of DCC reflectances.

## Slide 3
Current VIIRS DCC Methodology
Data Used
  SNPP (N20) VIIRS level 1B pixel radiances
DCC pixels selection criteria (no change)
  BT(11µm) < 205 K
  Spatial Homogeneity (
  SDV () < 1 K
  SZA and VZA < 40°
  tropical zone of 20 latitude
BRDFs
  Hu BRDF for the visible bands
  Ocean and Land empirical monthly BRDFs for each SWIR band
Stability monitoring statistics
  Use KDE instead of PDF to construct histograms
    Provides robust histograms for sparse DCC sampling
    PDF impacted by discretization errors
    Kernel density estimation (KDE) from the gaussian KDE function
  Use the KDE inflection point for the visible bands
  Use the mean statistic for SWIR bands
* Red text highlights the updated approach
VIIRS I1
AHI B3
Mean
Mode
Median
Inflection
Mean = average of the pixel radiances
Median = radiance where half of the pixels have a lower and higher radiance
Mode = radiance with the greatest frequency
Inflection point = radiance where the 2nd order derivative (curvature) sign changes usually near the half maximum

## Slide 4
KDE vs PDF statistics
• For visible bands the KDE mode and inflection point standard error are more stable than the PDF
• The KDE inflection point is the most stable KDE statistic
KDE
PDF
KDE

## Slide 5
Monthly Land-Ocean BRDF models
=
Derived by partitioning the DCC-identified pixel Radiance () into angular bins defined by 5° SZA, 5° VZA, and 10° relative azimuth angle (RAA) intervals
The reference angular condition chosen (SZA = 22.5°, VZA = 32.5°, RAA = 145°) represented the most frequently sampled angular conditions, ensuring robust statistical representation.
Where,
= BRDF corrected radiances after applying monthly BRDF
Where,
= BRDF corrected radiances after applying monthly land BRDF
= BRDF corrected radiances after applying monthly ocean BRDF.
Takes into account the brightness difference between land and ocean

## Slide 6
SE = 0.62%
SE = 0.21%
~66% reduction
SE = 1.7%
SE = 0.54%
~68% reduction
0.65 µm channel
No BRDF
1.61µm
No BRDF
0.65 µm channel
No BRDF
1.61 µm channel
No BRDF
1.61 µm
land/ocean BRDF
0.65µm
Hu BRDF
0.65µm
Hu BRDF
1.61 µm
Monthly land/ocean BRDF
Application of Hu and Land/Ocean BRDF models

## Slide 7
VIIRS channel | Standard error (%) |  |  |  |  |  |  | 
 | No BRDF |  |  |  | Hu model and land/ocean seasonal BRDFS |  |  | 
 | KDE mode | KDE mean | KDE median | KDE inflection | KDE mode | KDE mean | KDE median | KDE inflection
M3 | 0.57 | 1.00 | 0.83 | 0.67 | 0.35 | 1.03 | 0.81 | 0.25
M4 | 0.60 | 1.00 | 0.82 | 0.70 | 0.33 | 1.00 | 0.77 | 0.25
I01 | 0.58 | 0.99 | 0.80 | 0.73 | 0.31 | 1.00 | 0.76 | 0.24
M5 | 0.57 | 1.01 | 0.82 | 0.62 | 0.31 | 1.03 | 0.78 | 0.21
M7 | 0.48 | 0.93 | 0.69 | 0.51 | 0.25 | 0.97 | 0.64 | 0.23
M8 | 0.50 | 0.62 | 0.53 | 0.67 | 0.28 | 0.31 | 0.26 | 0.55
M9 | 1.29 | 1.36 | 1.31 | 1.27 | 0.82 | 0.65 | 0.61 | 1.70
I03 | 2.06 | 1.71 | 1.75 | 2.44 | 0.82 | 0.54 | 0.55 | 1.08
M10 | 2.04 | 1.70 | 1.74 | 2.43 | 0.81 | 0.54 | 0.55 | 1.00
M11 | 1.51 | 1.28 | 1.30 | 1.81 | 0.55 | 0.42 | 0.42 | 0.86
Trend standard errors (%) by KDE statistics
• Bold text indicates the lowest trend standard errors
• Mean and Median shows consistent SWIR band stability
<-Visible bands->
<-SWIR bands->

## Slide 8
The tropical land and ocean stratification was a simple solution to address their distinct radiative properties:
Examine the monthly 10° latitude-longitude regional DCC radiances
  To verify the Hu and land/ocean monthly BRDF model improvements
  Use January 2012 to July 2024 to build the monthly regional DCC dataset
  To increase sampling use a 3-month running mean to define each month
Incorporate a monthly 10° latitude-longitude regional BRDF for SWIR bands to improve the imager stability monitoring statistics
Monthly Regional DCC BRDF models

## Slide 9
Regional Monthly NPP 0.65µm DCC Reflectance
Mean
Mode
Inflection Point
No BRDF
NPP,Jan,M5
NPP,Jan,M5
NPP,Jan,M5
NPP,April,M5
NPP,April,M5
NPP,April,M5
NPP,July,M5
NPP,July,M5
NPP,July,M5
NPP,October,M5
NPP,October,M5
NPP,October,M5

## Slide 10
Regional Monthly NPP 0.65µm DCC Reflectance
Mean
Mode
Inflection Point
With Hu BRDF
NPP,Jan,M5
NPP,Jan,M5
NPP,Jan,M5
NPP,April,M5
NPP,April,M5
NPP,April,M5
NPP,July,M5
NPP,July,M5
NPP,July,M5
NPP,October,M5
NPP,October,M5
NPP,October,M5

## Slide 11
SE = 1.7%
1.61µm
No BRDF
1.61 µm channel
No BRDF
Application of Regional BRDF model SWIR bands
1.61 µm
land/ocean BRDF Monthly BRDF
SE = 0.54%
~68% reduction
1.61 µm
Monthly land/ocean BRDF
1.61 µm
Monthly regional BRDF
SE = 0.37%
~78% reduction

## Slide 12
Regional Monthly NPP 1.61µm DCC Reflectance
No BRDF
Land/ocean BRDF
KDE mean
monthly BRDF
Regional BRDF

## Slide 13
Trend standard errors summary
VIIRS channel | Standard error (%) |  |  |  |  |  | Improvements (% reduction) With Hu model
 | No BRDF |  | Hu Model |  | Regional BRDF |  | 
 | KDE mean | KDE inflection | KDE mean | KDE inflection | KDE mean | KDE inflection | 
M3 | 1.00 | 0.67 | 1.03 | 0.25 | 0.38 | 0.88 | 63%
M4 | 1.00 | 0.70 | 1.00 | 0.25 | 0.42 | 0.92 | 64%
I01 | 0.99 | 0.73 | 1.00 | 0.24 | 0.40 | 0.95 | 67%
M5 | 1.01 | 0.62 | 1.03 | 0.21 | 0.40 | 0.94 | 66%
M7 | 0.93 | 0.51 | 0.97 | 0.23 | 0.34 | 0.76 | 55%
VIIRS channel | Standard error (%) |  |  | Improvements (% reduction) With Regional BRDF
 | No BRDF | Monthly Land/Ocean BRDF | Regional BRDF | 
 | KDE mean | KDE mean | KDE mean | 
M8 | 0.62 | 0.31 | 0.21 | 66%
M9 | 1.36 | 0.65 | 0.47 | 65%
I03 | 1.71 | 0.54 | 0.37 | 78%
M10 | 1.70 | 0.54 | 0.37 | 78%
M11 | 1.28 | 0.42 | 0.3 | 77%

## Slide 14
Conclusions
Recent DCC characterization enhancements include
  Using a Kernel Density Estimation (KDE) or Gaussian smoothing function designed for limited sampled datasets to avoid discretization errors
  Using the PDF-inflection point and applying the Hu-BRDF model to monitor visible band stability providing NPP VIIRS C2.1 between 0.2% to 0.3% stability uncertainties
  Using the PDF-mean and applying monthly regional BRDFs to monitor SWIR band stability providing NPP VIIRS C2.1 between 0.2% to 0.5% stability uncertainties
The Hu-BRDF provided more consistent regional PDF-mode and PDF-inflection point radiances but did not improve the PDF-mean
  The Hu-BRDF works best for the brightest DCC radiances
The monthly regional BRDFs normalizes the DCC PDF-mean response by season and spatially and is viable due to the much smaller DCC inter-annual variability
  For visible bands the NPP VIIRS C2.1 PDF-mean stability is reduced from 1.0% to 0.4%
  For SWIR bands the NPP VIIRS C2.1 PDF-mean stability is reduced an additional 25% from the land/ocean BRDF

## Slide 15
Thank you !

## Slide 16
NPP,Jan,M5
NPP,Jan,M10
NPP,Jan
NPP,April,M5
NPP,April,M10
NPP,April
NPP,July,M5
NPP,July,M10
NPP,July
NPP,October,M5
NPP,October,M10
NPP,October
Regional Monthly NPP 1.61µm DCC Reflectance
0.65µm Std Dev
Frequency
1.61µm Std Dev