## Slide 1
Update on SNO/Vicarious Calibration Focus Group
Tim Hewison
EUMETSAT
19/03/2025

## Slide 2: Update on SNO/Vicarious Calibration Focus Group
CGMS Action on MWSG
Focus Group Meetings 2024/2025
SNO Algorithm Development
  Dynamic Range v Resolution
  Top Hat v Actual SRFs in RTM
Vicarious Inter-Calibration
  Algorithm development
  Warm End Histogram method
Merging Focus Groups?

## Slide 3: Update on SNO/Vicarious Calibration Focus Group
CGMS Action on MWSG
Focus Group Meetings 2024/2025
SNO Algorithm Development
  Dynamic Range v Resolution
  Top Hat v Actual SRFs in RTM
Vicarious Inter-Calibration
  Algorithm development
  Warm End Histogram method

## Slide 4: CGMS Microwave Action on GSICS
CGMS-51 WG-II Action on GSICS: (April 2023)
  “Establish a methodology to characterise microwave instruments for O2 absorption channels through the SNO and RTM modelling.
  The implementation will be done successively by the individual satellite operators.”
  Status at CGMS-52 (April 2024):
    To be addressed at WGII IS#1 on 17 Sep 2024
    2024 January: GSICS to nominate new 'rapporteur’ to discussion on-going actions – who?
EUMETSAT is implementing SNO and NWP bias monitoring method
  as part of Cal/Val Plans for AMSU-A, MWS, MWI and EPS-Sterna
  through internal developments and partnerships with partner agencies
Can GSICS coordinate these methods among satellite operators?
  Agree common baseline algorithms?

## Slide 5: Update on SNO/Vicarious Calibration Focus Group
CGMS Action on MWSG
Focus Group Meetings 2024/2025
SNO Algorithm Development
  Dynamic Range v Resolution
  Top Hat v Actual SRFs in RTM
Vicarious Inter-Calibration
  Algorithm development
  Warm End Histogram method

## Slide 6: Review of SNO/Vicarious Focus Group Meetings 2024/25
2024-05-02
  Introducing SNO Focus Group and review of previously published algorithms
2024-08-08
  Progress with review of SNO methods
  Quantify differences between centres of Collocation Areas
2025-01-16
  Yang Guo (CMA) - SNO algorithm implemented for MWHS-II on FY-3F
  Tim Hewison (EUMETSAT) - Dynamic range v spatial resolution and Top Hat v Real Spectral Responses Katherine Wentz (RSS) - Absolute Intercalibration of Spaceborne Microwave Radiometers, focusing on vicarious methods using open ocean and rainforests
Not all presentations/discussions on GSICS Wiki!

## Slide 7: Update on SNO/Vicarious Calibration Focus Group
CGMS Action on MWSG
Focus Group Meetings 2024/2025
SNO Algorithm Development
  Dynamic Range v Resolution
  Top Hat v Actual SRFs in RTM
Vicarious Inter-Calibration
  Algorithm development
  Warm End Histogram method

## Slide 8: SNO Algorithm Development
Review of published SNO methods
  Ongoing
Developing SNO uncertainty framework
  Characterising spatial variability
  Using high-resolution Sentinel-6/AMR data (1D)
  Simulating 2D data: Structured Random Fields
  Contribution to uncertainty analysis
  Alternative: Possible use of simulations from NWP models?
Optimising SNO algorithm for test cases
  Defining Dynamic Range requirement
  Application to AWS test data starting March 2025
  Extension to “warm SNOs” (OCTM method)
  Applying uncertainty framework
Sterna Inter-Calibration Study
  With Deimos/UPC
  OCTM & Vicarious Inter-Calibration
  See agenda item 7k at 2025 Annual Meeting
Lukas Muser
  EUMETSAT Fellow at DWD, Germany
  investigating effects of inhomogeneities within satellite footprints
  Aims to enhance accuracy of data assimilation by understanding and characterizing observation errors
  Using NWP Model fields from ICON
  To simulate satellite microwave radiometer scenes
  up to 500m resolution
  1. Investigate inhomogeneities using simulated data
  2. Compare stats for different resolutions
  3. Compare difference to O-B stats
  4. Determine situation-dependent error description
  Relevant to SNO uncertainty
  Invite to MWSG web meeting

## Slide 9: Further SNO development
Yang Guo (CMA) - SNO algorithm implemented for MWHS-II on FY-3F
  Based on the work published in 2024: https://ieeexplore.ieee.org/document/10658988
  Comparison of collocated near-nadir observations with ATMS
  dt<15min
  ds<3km
  VZA<±5°
Compare thresholds used
  in review of published SNO methods
  Impact on uncertainty of relative biases

## Slide 10: Update to SNO Literature Review Spreadsheet
SharePoint Spreadsheet
  Linked here
  Snapshot here =>
Reviewing published SNO algorithms
Also Includes limited review of
  Vicarious inter-calibration
  NWP Double-Difference
Following previous discussion:
Added columns for
  Collocation Area
  Spectral Band / View Angle Adjustment Factor
    SBAF/VAAF
    Unpopulated so far!
Contributions welcome!
Class | Reference | Collocation Area (km) | ds (km) | dt (s) | dVZA (°) | VZAmax (°) | Method | Filter | SBAF /VAAF | L | C | X | K | V | W | F | D | G | H | J | Applicable Sensors
 |  |  |  |  |  |  |  | incl azi angle | Spectral/View adj. | 1.4 | 6.8 | 10.65 | 12-40 | 50-60 | ~89 | ~118 | ~157 | ~183 | ~229 | ~325 | 
Temp Sounders | Zou et al. 2006 | 1x1 | 111 | 100 |  | 5° | SNO |  |  |  |  |  |  | X |  |  |  |  |  |  | MSU Ch2
Temp Sounding | Iacovazzi & Cao, 2007 | 4SDP x 5TDP | 100 | 30 |  | 5° | SNO + bilinear Interp. |  |  |  |  |  | a | X | a |  | a | a |  |  | AMSU-A
 | Iacovazzi & Cao, 2008 | 4SDP x 5TDP | 100 | 30 |  | 5° | SNO + bilinear Interp. | SD<3xNEdT |  |  |  |  | X | X | a |  | a | a |  |  | AMSU-A, ATMS
Temp Sounders | Zou and Wang 2011 | 1x1 | 45 | 50 |  | 5° | SNO |  |  |  |  |  |  | X |  |  |  |  |  |  | AMSU-A , ATMS
Temp+ Humidity Sounding | Ackermann 2020 | 1SDP x 1TDP | 10 | 30 | 10° 3.6° | 10° | SNO + B-G resample |  |  |  |  |  | X | X | X |  | X | X |  |  | AMSU-A AMSU-B+MHS
Humidity Sounding | Moradi et al. 2015 |  | 50 | 3600 |  | Nadir | SNO |  |  |  |  |  |  |  |  |  |  | X |  |  | ATMS SAPHIR
 | John et al. 2012 | 3SDP x 3TDP | 5 | 300 |  | 3.9° | SNO |  |  |  |  |  |  |  |  |  |  | X |  |  | MHS
 | EUMETSAT MHS FCDR 2023 |  | 10 | 300 3600 | 5% | 15° | SNO | SD(3x3)<NEDT *sqrt(2) |  |  |  |  |  |  |  |  |  | X |  |  | MHS
 | Dou et al. 2022 | 1SDP x 1TDP | 3 | 1200 |  | 5° | SNO | +SD(3x3)<1K |  |  |  |  |  |  |  |  |  | X |  |  | MWHS-MHS
 | Xie et al, 2024 | 1SDP x 1TDP | 3 | 900 |  | 5° | SNO |  |  |  |  |  |  |  |  |  |  | X |  |  | MWHS2-ATMS
Window SNO | Yan & Weng, 2008 | 1SDP x 1TDP | 12.5 | 60 |  | All | SCO | SD<1K |  |  |  |  | X | X | X |  |  |  |  |  | SSMIS-SSM/I
 | Song Yang et al., 2011 |  | 3 | 120 |  | All | SCO | SD<2K, ¦dTb¦<10K |  |  |  |  | X |  | X |  |  |  |  |  | SSM/I
 | Zou et al. 2014 |  | 15 | 60 |  |  | SNO + B-G resample | +1-sigma |  |  |  |  | X | X | X |  |  |  |  |  | AMSU-ATMS
 | Yang et al., 2020 "IMICA" | 2SDP x 1TDP | 50-75 | 50 |  | 3.3° | SNO | +SD |  |  |  |  | X |  | X |  |  |  |  |  | AMSU-A
 | Yan et al., 2020 |  | 30 | 80 |  |  | SNO | +SD<2K |  |  |  |  | X | X | X |  |  |  |  |  | AMSU
Generic SNO | Hewison 2023 - Proposal for Sterna inter-calibration (STC) |  | 7.5 | 900 | 5° /1?° | 5° /55?° | SNO+OCTM /SCO |  | SBAF /TBD |  |  |  |  | X | X |  | X | X |  | X | Sterna-MWS/ATMS Sterna-ICI

## Slide 11: Update on SNO/Vicarious Calibration Focus Group
CGMS Action on MWSG
Focus Group Meetings 2024/2025
SNO Algorithm Development
  Dynamic Range v Resolution
  Top Hat v Actual SRFs in RTM
Vicarious Inter-Calibration
  Algorithm development
  Warm End Histogram method

## Slide 12: Vicarious Inter-Calibration algorithm development
Katherine Wentz (RSS) - Absolute Intercalibration of Spaceborne Microwave Radiometers
  Based on the work published in 2024: https://doi.org/10.1175/JTECH-D-24-0024.1
  Comparisons of microwave imagers over stable areas: Open Ocean & Amazon rainforest
  Using GPM Microwave Imager (GMI) as reference instrument
  Based on binning obs within 1h time window on 0.25° grid
  Used to derive 3 calibration parameters
    (non-linearity, beam spillover & cross-polarisation)
  Only uses RTM for SBAF
  Impressive performance
  Highlighted benefit of comparing performance in ascending/descending parts of orbit
Histogram Warm End Vicarious Calibration –
  Rachael Kroodsma found stable high Tb cutoff in O-B warm histograms [IGARSS 2018 proceedings paper + poster]
EUMETSAT Study on use of Radiosondes for Vicarious Calibration of MWI/ICI
  sub-millimetre channels with no inter-calibration reference instrument
  See 2025 GSICS Annual Meeting – agenda item 7m

## Slide 13: Update on SNO/Vicarious Calibration Focus Group
CGMS Action on MWSG
Focus Group Meetings 2024/2025
SNO Algorithm Development
  Dynamic Range v Resolution
  Top Hat v Actual SRFs in RTM
Vicarious Inter-Calibration
  Algorithm development
  Warm End Histogram method
Plan for 2025/2026
Notes: from Ed Kim to Tim Hewison (privately)
13:36Thrilled to see these focus groups. [I've missed the last few GSICS meetings.] Have the groups decided on definitions of 'inter-calibration' and 'inter-comparison'? If not, I strongly recommend following the lead of our national standards organizations (e.g, NPL, NIST,..) and not the what our precip colleagues call 'inter-cal.' I believe this is consistent with Eumetsat, CIMR. I know it is consistent with SMBA. Adopting rigorous uncertainty & traceability paradigms is also a big improvement. CIMR already does. The Eumetsat Conference has entire sessions on the topic. I'm even seeing some NASA science programs that aren't doing spaceflight adopt it. Our VIS/IR/thermal IR colleagues have been doing this for up to 2 decades. The train has left the station; the mw radiometer community would do well to be on board.

## Slide 14: Lessons from developing GSICS IR products
Build on existing developments, where possible:
  Look at what has already been done and consider re-use
  GSICS Data and Products Servers, GSICS File name convention
  GSICS Procedure for Product Acceptance – Maturity Index – iterative peer review process
Consider use case:
  Monitoring calibration of operational missions
  Calibration corrections – for NRT, case studies (RAC), Archive re-calibration of single/multiple missions (FCDRs)
  Make it easy to use – consider integration into satpy readers
  Best practices – who for?
Keep it Generic
  Think ahead – to other channels, instruments, …
  Don’t hard code options and assumptions – variable names, correction formulae
Start simple – but start now!
  E.g. start with a strawman algorithm
  Identify issues with the algorithm and work in teams to solve
  Agree a common baseline algorithm
  Aim to iterate – e.g. tuning baseline algorithm for particular applications, instruments, …
  Draft manuscripts collaboratively – really helps identify little differences
Agree a community reference for inter-calibration products
  Agree ways to compare references
  Consider combining where possible (consistent)

## Slide 15: SNO/Vicarious Calibration Focus Group Plan for 2025/26
Review IPWG inter-calibration requirements
  and current algorithms
Consolidate proposal for a baseline SNO algorithm
  and uncertainty framework
  for independent evaluation by different groups – with different sensors
Continue Review of other vicarious (inter-)calibration algorithms
  Inviting experts to present at web meetings

## Slide 16: Update on SNO/Vicarious Calibration Focus Group
CGMS Action on MWSG
Focus Group Meetings 2024/2025
SNO Algorithm Development
  Dynamic Range v Resolution
  Top Hat v Actual SRFs in RTM
Vicarious Inter-Calibration
  Algorithm development
  Warm End Histogram method
Merging Focus Groups?
Notes: from Ed Kim to Tim Hewison (privately)
13:36Thrilled to see these focus groups. [I've missed the last few GSICS meetings.] Have the groups decided on definitions of 'inter-calibration' and 'inter-comparison'? If not, I strongly recommend following the lead of our national standards organizations (e.g, NPL, NIST,..) and not the what our precip colleagues call 'inter-cal.' I believe this is consistent with Eumetsat, CIMR. I know it is consistent with SMBA. Adopting rigorous uncertainty & traceability paradigms is also a big improvement. CIMR already does. The Eumetsat Conference has entire sessions on the topic. I'm even seeing some NASA science programs that aren't doing spaceflight adopt it. Our VIS/IR/thermal IR colleagues have been doing this for up to 2 decades. The train has left the station; the mw radiometer community would do well to be on board.

## Slide 17: Thoughts on further merging of MWSG Focus Groups
Follow up on Proposal to merge the following three focus groups
  Direct MW Radiometer Inter-comparison Method
  MW Radiometer Vicarious Calibration
  Radiative Transfer Model (RTM) Facilitated MW Radiometer Inter-calibration
Complimentary inter-calibration methods
  Focus on different channels & applications
  Different expertise – original motivation for focus groups
Not all focus group presentations/discussions on GSICS Wiki!
  Difficult to keep track of decisions, progress…
  Proposals:
    to invite whole MWSG mailing list to focus group meetings – reduce duplication
    Focus Group leads to consolidate Sub-Group progress report at annual meeting