## Slide 1: Progress of Microwave Radiometer Direct Inter-Calibration (“SNO”) Method Focus Group 2024-08-28 Microwave Sub-Group Meeting
Focus Group Members
Cheng-Zhi Zou (NOAA)
Flavio Iturbide (NOAA)
Siena Iacovazzi (GST @ NOAA)
Tim Hewison (EUMETSAT)
Yang Guo (CMA)
+ Your contributions are welcome!

## Slide 2: Presentation – see below
I shared ideas to expand the review of existing SNO methods
  (see SharePoint spreadsheet).
We agreed:
  It is important to be clear which is used,
    and use data after Antenna Pattern Correction, if possible
  to note any azimuth angle constraints under “Filters” column is spreadsheet
  to add column for Spectral/Geometric Corrections in spreadsheet
  to aim to provide “Recipe” for how to define SBAFs/GAFs
    as part of recommended SNO algorithm
I shared an analysis of the variograms from Sentinel-6/AMR
  to evaluate uncertainty contributions from spatial variability and mis-aligned SNOs

## Slide 3: Discussions
Siena shared details of a complementary approach to characterise the uncertainty on SNOs
  Iacovazzi and Cao, 2008: https://doi.org/10.1175/2007JTECHA1020.1
  due to spatial variability of constituent pixels
  relative to NEDT
  ratio increase by 2 orders of magnitude from sounding to window channels
  used as a basis for rejecting SNOs with excessive spatial variability
We discussed the potential benefit of adopting a weighted averaging approach instead
  This could also provide an uncertainty on the mean SNO bias
  Would be interesting to compare with expectations from variogram analysis
We discussed ideas to characterise temporal variability
  E.g. using data from static balloons or special aircraft manoeuvres

## Slide 4: Development Plans
Plans to implement SNO methods
I shared plans to implement SNO method based on EUMETSAT MHS FCDRs to inter-calibrate data from ESA Arctic Weather Satellite (AWS) with ATMS and AMSU-A/MHS.
Hope to have results to share in Fall 2024
Siena may also have other results to share then
Aim for next meeting then
AOB:
Link to ECMWF Bias Monitoring pages via NWP SAF:
  https://nwp-saf.eumetsat.int/site/monitoring/nrt-monitoring/
  Includes links to monitoring pages from UKMO, MeteoFrance, NCEP and others

## Slide 5: Discussions in 2024-08-28 Meeting
Use of many collocations
  Trade-off uncertainty of each SNO,
  number of SNOs,
  dynamic range and
  frequency with which calibration updates can be provided
Dealing with asymmetry in collocations:
  E.g. biases due to small differences in viewing angle
    These can be included in Geometric Correction Factor
  Important to include check that collocations are symmetric in ATBD!
  Tim to consider whether this can be included in variogram analysis

## Slide 6
Slides presented at SNO Focus Group meeting 2024-08-08
With some updates!

## Slide 7: Review Existing SNO Methods*
Started Shared Spreadsheet
Summarising basic elements of different SNO Methods
  Based on publications over the last 20 years
  Collocation area - area over which observations are compared
  Collocation criteria:
    ds (km) - Maximum separation between collocation centres
    dt (min) - maximum time difference between instruments
    dVZA(°/%) - maximum difference in Viewing Zenith Angle
    VZAmax(°) - maximum VZA
  Basic Method, Filters, Applicable Spectral Bands & Instruments
* Review includes some NWP Double-Difference and Vicarious Inter-calibration methods – please feel free to copy!

## Slide 8: Snapshot of Spreadsheet

## Slide 9: Since last meeting 2024-05-02
From “Notes” tab in spreadsheet:
Added 118GHz and 229GHz bands to spreadsheet
  Agreed further bands could be added later if needed
Agreed to include any uncertainty assessments published for methods
  Aim to develop generic uncertainty analysis for SNO methods
Terminology
  Agreed “Collocation Area”
  SDP = Scan-Direction Pixels x TDP = Track-Direction Pixels
  Need to complete details of Collocation Areas for more methods – all 1x1?
Added new worksheet to show regions covered by SNOs from different sensor combos

## Slide 10: Open Questions for SNO review + answers
Do we need to include azimuthal angle constraints?
  Often not used in microwave SNOs – especially near nadir
  Useful for window channels? E.g. for conical imagers?
  Agreed to note any constraints under “Filters” column is spreadsheet
Do we need to review any Spectral Band Adjustment Functions?
  Used in published algorithms to account for SRF differences
And “Geometric Adjustment Functions”?
  To account for systematic differences in viewing angle/polarisation
  E.g. to compare different conically-scanning microwave imagers
  Agreed to add column for Spectral/Geometric Corrections in spreadsheet
  Aim to provide “Recipe” for how to define SBAFs/GAFs – as part of recommended SNO algorithm
How to account for antenna patterns?
  Or just compare antenna temperatures? Noted instruments with different sidelobes can appear biased
  Agreed important to be clear which is used, and use data after Antenna Pattern Correction, if possible

## Slide 11: Example Collocation Areas

## Slide 12: Towards Uncertainty Analysis
Quantify differences between centres of Collocation Areas
  + Scale spatial variability accordingly?
  Statistics from aircraft measurements – e.g. COSMIR on ER-2 ~1km²
E.g. analysis of Sentinel-6/AMR data…
  1-D case

## Slide 13: Spatial Variability from S6/AMR
Channel/GHz | 18.7 | 23.8 | 34 | 89 | 130 | 166
Bandwidth/MHz | 200 | 400 | 700 | 5000 | 5000 | 5000
NEDT | 0.13? |  |  | <0.1 | <0.1 | <0.1
Swath | Nadir only |  |  | Nadir+x° only |  | 
FWHM/km | 40 | 34 | 31 | 5 | ~4 | ~3
Sampling/Hz | 16/8 |  |  | 16 |  | 
Sampling/km | 0.36/0.72 |  |  | 0.36 |  | 
Sentinel-6 “Michael Freilich” Orbital Characteristics (ref) | 
Type | non-synchronous
Altitude | 1336km
Inclination | 66.039°
Repeat cycle | 9.9156 days
Ground track velocity | 5.8 km/s
High spatial sampling (up to 360m)
High radiometric resolution (TBC)
But 1-D sampling only!
Not in protected bands – prone to RFI
1 month coverage (2024-05)

## Slide 14: Example of RFI at 34GHz
Not all bands protected
34GHz prone to RFI
Not always flagged as bad radiometric quality
Only use unflagged data from now…

## Slide 15: Variogram Analysis
Evaluate variability
Using Variograms
RMSD of Tb differences sampled over various intervals
  In time
  Equivalently, space
Slope=5/3
  Kolmogorov cascade
  Turbulent sub-range?
Noise Floor

## Slide 16: SNO Uncertainty due to spatial variability
How much uncertainty on collocation due to misalignment?
Plotted on linear scale
E.g. 50 samples = 18km,
  SQRT(variogram) ~4K
At 10 samples = 3.6km,
  SQRT(variogram) ~1K
Includes ocean & land
  Clear & cloudy
Only 1-D
  Repeat with 2-D data
  LPF to mimic larger FOV

## Slide 17: Expected Temporal Variogram
log(lag(time))
Log(Semi-variogram)
Nugget (Noise)
Effective Range (95% sill)
Diurnal Variations (12h max, 24h min)
Seasonal Variations (6m max, 1y min)
Convective
Scale ~1min

## Slide 18: Expected Spatial Variogram
log(lag(distance))
Log(Semi-variogram)
Nugget (Noise)
Effective Range (95% sill)
Synoptic
Scale ~300km
Global Scale (10000km max, 20000km min)
Convective
Scale ~1km

## Slide 19: Generate Synthetic 2-D Image
From Variogram
Used to evaluate uncertainty
  For different collocation areas
  Overlaps with various lags

## Slide 20: SNO Uncertainty due to temporal variability
In principle can analyse temporal variability
  in same way as spatial
But don’t have MWRs staring at same scene
Could use balloon-borne radiometers?
Could use aircraft observations
  E.g. when flying in a circle, observing at an angle
  In discussion with NASA-GSFC for ER-2/COSMIR
  As part of WH²yMSIE campaign Oct/Nov 2024

## Slide 21: AWS
AWS = Arctic Weather Satellite
ESA’s New small satellite
Earth Watch Programme Element
50-57, 166, 183, 325 GHz
Launched 2024-08-16
Plan to implement EUMETSAT MHS FCDR SNO algorithm for AWS data
Compare with ATMS, AMSU-A/MHS
Data From October 2024

## Slide 22: Post-meeting Additions
Backup slides showing some details of Further analysis…

## Slide 24
Channel (GHz) | 18.7 | 23.8 | 34 | 89 | 130 | 166
NEDT | 0.13? |  |  | <0.1 | <0.1 | <0.1
FWHM (km) | 40 | 34 | 31 | 5 | ~4 | ~3
Sampling (Hz) | 16/8 |  |  | 16 |  | 
Sampling (km) | 0.36/0.72 |  |  | 0.36 |  | 
Shaded areas:
Max lag=FWHM
Min lag =Departs from 5/3
Thin black line:
- fit to >FHWM by eye