## Slide 1: LIME: Lunar Irradiance Model of ESA Pieter De Vis​ (NPL), Stefan Adriaensen (VITO), Africa Baretto (UVa), Agnieska Bialek (NPL), Marc Bouvet (ESA), Javier Gatón (UVa), Ramiro Gonzalez (UVa), Carlos Toledano (UVa) 13/11/2025 - GSICS Lunar Calibration Subgroup meeting

## Slide 2: LIME: Lunar Irradiance Model of ESA
Derived using SI-traceable CIMEL measurements at Teide Peak and Izaña Observatory in Tenerife
Characterization and calibration at NPL and University of Valladolid
LIME model (ROLO-based) fitted at CIMEL wavelengths
Spectral interpolation using lunar ASD measurements
Uncertainty computation based on Monte Carlo simulations accounting for calibration, modelling and measurement uncertainties
LIME-TBX allows to simulate lunar observation and perform comparisons

## Slide 3: GSICS comparison of lunar models (T. Stone)
Just one example of the comparisons performed by T. Stone and lunar modellers in the frame of GSICS

## Slide 4: Timeline
After SI-traceable calibration at NPL, the CIMEL instrument is deployed in Tenerife, and starts taking lunar measurements.
CIMEL measurements
During 2022, three field campaigns were undertaken to take hyperspectral measurements with an ASD spectrometer. These are used for spectral interpolation of the LIME model
ASD measurements
Paper describing the LIME model is published. CIMEL data from 2018-2022 is used. Includes description of measurements, calibration, model fitting, uncertainties and comparisons.
Toledano et al. (2024)
DOLP and AOLP model added to LIME-TBX, based on measurements taken with different polarization filters.
Polarisation added
An adapted version of the ROLO lunar model is fitted to the CIMEL data. Uncertainties are propagated through the fitting process.
ROLO model fitted
V1.0.0 of the LIME-TBX is released. The LIME toolbox allows to simulate output of the model and compare these to actual lunar observations.
LIME-TBX v1 released
The LIME website is online.
https://lime.uva.es/
Access LIME-TBX installers, documentation, forum, …
LIME website
March 2018
2022
Mar 2024
Mar 2025
2018 - 2019
Dec 2023
June 2024
LIME 2 CCN Mar 2024 – Oct 2025
LIME 2 Oct 2021 – Feb 2024
LIME Sep 2017 – Dec 2019
Maintenance contract for CIMEL measurements and coefficients 2019 – 2027
Oct 2025
The latest version of the LIME-TBX is released, including updated coefficients, spectral interpolation and DOLP/AOLP model
LIME-TBX v1.4 released

## Slide 5: The LIME measurements
CIMEL 318-TP9

## Slide 6: Irradiance Responsivity
Spectral Channel | Calibration Coefficient (MOON gain) | Standard uncertainty
440 nm Si | 5.759 × 10-10 | 0.97%
500 nm Si | 4.481 × 10-10 | 0.96%
675 nm Si | 3.205 × 10-10 | 0.92%
870 nm Si | 2.547 × 10-10 | 0.91%
937 nm Si | 2.431 × 10-10 | 0.97%
1020 nm Si | 2.735 × 10-10 | 1.05%
1020 nm InGaAs | 2.119 × 10-10 | 1.01%
1640 nm InGaAs | 4.893 × 10-11 | 1.06%

## Slide 7: New CIMEL channels used in LIME
New LIME channels: 1240, 1550, 2060, 2130 nm
Insufficient data so far to provide model coefficients.

## Slide 8: Lunar disc irradiance measurements

## Slide 9: Lunar Irradiance Model
= model spectral band
= lunar reflectance
= absolute phase angle [radians]
= selenographic latitude of observer [degrees]
= selenographic longitude of observer [degrees]
= selenographic longitude of the Sun [radians]
Lunar irradiance measurements at 440 nm based on more than 3+ years of measurements
Based on Kieffer and Stone (2005)​

## Slide 10: Uncertainty Analysis
Monte Carlo approach is used to propagate uncertainties, taking into account error-correlations
CoMet toolkit used for uncertainty propagation using 1000 MC iterations
Includes random measurement uncertainties, systematic instrument uncertainties, regression uncertainties & interpolation uncertainties
 | Langley points | Nights | Spectral
Calibration | C | C | PC
Instrument Noise | I | I | I
Temperature | C | I | C
Aerosol variability | PC | I | C
C = correlated; I = independent; PC = Partially correlated
Notes: 𝐸_(𝑖,𝜆)^"True" is the nominal “true” value for the TOA irradiance in spectral band 𝜆 for the 𝑖th observation
𝑅_(𝑖,𝜆) is the error in the observation in spectral band 𝜆 for the 𝑖th observation due to random effects, expressed in relative terms, e.g. as a percentage of the true value
𝑆_𝜆 is the error in the observation that is common for all measurements in this band, expressed in relative terms, e.g. as a percentage of the true value
𝐶 is the error in the observation that is common for all measurements in all bands, expressed in relative terms, e.g. as a percentage of the true value
The error values are unknown; but are draws from a probability distribution with a standard deviation given by the relative uncertainty associated with this effect and with an expectation value (central value) of zero.
𝑅_(𝑖,𝜆) takes a different value for every observation. This comes from random processes relating to the measurement of the TOA irradiance for a particular night. These include instrument noise, instrument temperature changes and atmospheric changes – and relates to the relative uncertainty in the Langley Plot intercept that is estimated above [section 0].

## Slide 11: LIME-TBX Spectral interpolation
Aim is to extend LIME from the CIMEL wavelengths to 350-2500 nm
ASD measurements or Apollo spectrum can be used for spectral interpolation in LIME-TBX
ASD measurements reveal variation of spectral slope with phase angle
Reference dataset is rescaled to go through the LIME model reflectances at CIMEL wavelengths using CoMet toolkit
Combines relative accuracy of ASD with absolute accuracy of CIMEL

## Slide 12: Lunar hyperspectral reflectance measurements
Thermally controlled ASD spectrometer
Foreoptics with optical fiber.
Improved foreoptics were developed as part of LIME 2 CCN
Neutral density filter to measure solar irradiance
Sun/moon tracker

## Slide 13: New foreoptics ASD
Köhler illumination
Acromat doublet
Aperture

## Slide 14: Preparing ASD spectral interpolation dataset
ASD measurements were taken over 4 months in 2022 and 2 months in 2025
Measurements in absorption features are too noisy and are omitted
Replace masked data with rescaled Apollo spectrum using comet_maths
Data divided in bins of 10° spanning -95° to 95°
Linearly interpolated with phase angle to phase angles required within the LIME-TBX
Stored as NetCDF file for use within LIME-TBX

## Slide 15: Preparing ASD spectral interpolation dataset
ASD measurements were taken over 4 months in 2022 and 2 months in 2025
Measurements in absorption features are too noisy and are omitted
Replace masked data with rescaled Apollo spectrum using comet_maths
Data divided in bins of 10° spanning -95° to 95°
Linearly interpolated with phase angle to phase angles required within the LIME-TBX
Stored as NetCDF file for use within LIME-TBX

## Slide 16: Preparing ASD spectral interpolation dataset
ASD measurements were taken over 4 months in 2022 and 2 months in 2025
Measurements in absorption features are too noisy and are omitted
Replace masked data with rescaled Apollo spectrum using comet_maths
Data divided in bins of 10° spanning -95° to 95°
Linearly interpolated with phase angle to phase angles required within the LIME-TBX
Stored as NetCDF file for use within LIME-TBX

## Slide 17: Preparing ASD spectral interpolation dataset
ASD measurements were taken over 4 months in 2022 and 2 months in 2025
Measurements in absorption features are too noisy and are omitted
Replace masked data with rescaled Apollo spectrum using comet_maths
Data divided in bins of 10° spanning -95° to 95°
Linearly interpolated with phase angle to phase angles required within the LIME-TBX
Stored as NetCDF file for use within LIME-TBX

## Slide 18: Preparing ASD spectral interpolation dataset
ASD measurements were taken over 4 months in 2022 and 2 months in 2025
Measurements in absorption features are too noisy and are omitted
Replace masked data with rescaled Apollo spectrum using comet_maths
Data divided in bins of 10° spanning -95° to 95°
Linearly interpolated with phase angle to phase angles required within the LIME-TBX
Stored as NetCDF file for use within LIME-TBX

## Slide 19: Preparing ASD spectral interpolation dataset
Dataset available on Zenodo
https://doi.org/10.5281/zenodo.10534235
ASD measurements were taken over 4 months in 2022 and 2 months in 2025
Measurements in absorption features are too noisy and are omitted
Replace masked data with rescaled Apollo spectrum using comet_maths
Data divided in bins of 10° spanning -95° to 95°
Linearly interpolated with phase angle to phase angles required within the LIME-TBX
Stored as NetCDF file for use within LIME-TBX

## Slide 20: Degree of Linear Polarisation measurements
Coyne et al, 1969
LIME DOLP

## Slide 21
LIME toolbox: lunar irradiance / DoLP simulations
Simulates:
  Irradiance
  Band-integrated Irradiance (Signal)
  Reflectance
  Degree of linear polarisation
  Angle of linear polarisation

## Slide 22: Reflectance & Irradiance Simulation

## Slide 23
Input:
  Geographic coordinates & datetime/s
  Selenographic coordinates
  Satellite name & datetime/s
    User may add satellites if they have .tle or .osf files.
  Optional: SRF file in GLOD format
LIME toolbox: lunar irradiance / DoLP simulations

## Slide 24
LIME toolbox: simulation vs. observation comparisons

## Slide 25: Coefficients & Settings
Select & Download updated LIME coefficients
Modify interpolation options

## Slide 26: Command-Line Interface (CLI)

## Slide 27: CIMEL

## Slide 28: CIMEL

## Slide 29: PROBA-V

## Slide 30: PLEIADES

## Slide 31: S3B-OLCI

## Slide 32: AIR-LUSI (2019)

## Slide 33: AIR-LUSI (2022)

## Slide 34: LIME website: lime.uva.es
LIME
Toolbox
Lunar
Datasets
Project
Documents
Downloads

## Slide 35: Conclusions
LIME modelling now based on 7+ years of continuous lunar measurements
Further measurements secured until 2027
Hyperspectral ASD measurements provide info on spectral shape, and are anchored to LIME model at CIMEL wavelengths
LIME-TBX allows to simulate output of the model and compare these to actual lunar observations.
Comparisons carried out and documented against various sensors
Continuous efforts to keep improving measurement quality and modelling
The measurements, the LIME toolbox and the associated documentation are available on LIME website and ESA Cal/Val portal

## Slide 36: Thank you!
pieter.de.vis@npl.co.uk
https://lime.uva.es/
http://calvalportal.ceos.org/lime