## Slide 1
LSICS status
Sébastien Wagner
Remote Sensing Scientist – Radiometric Calibration
GSICS VNIR web meeting / 13.11.2025

## Slide 2: The LSICS project
  LSICS = activity within the GSICS Lunar Calibration subgroup
  Development group, roles and responsabilities:
    Project leader / coordinator : T. Stone (USGS)
    Main developers : NOAA (Biskash Basnet) till December 2024 / EUMETSAT (Seb Wagner with support from Vincent Debaecker) since January 2025
    Support: JMA (Masaya Takahashi), NOAA (Fangfang Yu, Fred Wu – till December 2024), Celestial Reasoning (Hugh Kieffer), Earth Space Solutions (Matthijs Krijger)
  Coordination and meetings:
    Regular meetings (every 2 or 3 weeks)
    Minutes are available
  Infrastructure
    Gitlab repository with main and development branch hosted by EUMETSAT
      “Main” to host the official version to be used
      “Development” branch for enhancements / new functionalities development and testing
      Project still in restricted access (version v1.0.0 in preparation)
    Confluence page made available by EUMETSAT but currently not used by the group  option still available if need arises

## Slide 3: Development status
Main functionalities for LSICS have been implemented
  SLIMM model
  Modular approach to integrate additional models
  Standard input / output formats
  Functionality to feed LSICS with GIRO input files  integrated converter
  SRF files following the GSICS SRF format (GIRO compatible)

## Slide 4: How does LSICS work?
Input
Dynamic configuration file
Static configuration file
Observations (GIRO/LSICS)
GIRO_INPUT defined
Ingest GIRO input
Operation: concatenate the GIRO records in one LSICS file
Global attributes as required by LSICS
History
Variables as required by LSICS
LSICS input
Yes
No
Ingest and Geometry Calculation Module
Operation: compute Lunar Observation Angle Set (LOAS)
• Phase angle (signed)
• Sub-solar longitude and latitude
• Sub-observer longitude and latitude
LOAS output
Lunar Disk Reflectance Module
Operation: compute lunar disk equivalent reflectance spectra
• set up basis functions
• reconstruct disk reflectance model
• compute model on operating wavelenghts
Model Definitions
• Operating wavelength set
• Basis function coefficients
DER output

## Slide 5: How does LSICS work?
Input
Dynamic configuration file
Static configuration file
Observations (GIRO/LSICS)
GIRO_INPUT defined
Ingest GIRO input
Operation: concatenate the GIRO records in one LSICS file
Global attributes as required by LSICS
History
Variables as required by LSICS
LSICS input
Yes
No
Ingest and Geometry Calculation Module
Operation: compute Lunar Observation Angle Set (LOAS)
• Phase angle (signed)
• Sub-solar longitude and latitude
• Sub-observer longitude and latitude
LOAS output
Lunar Disk Reflectance Module
Operation: compute lunar disk equivalent reflectance spectra
• set up basis functions
• reconstruct disk reflectance model
• compute model on operating wavelenghts
Model Definitions
• Operating wavelength set
• Basis function coefficients
DER output
Spectral Irradiance Module
Operation: produce model irradiances in sensor bands
• Convolve disk reflectance, solar irradiance and SRF
• Apply distance corrections
Reference Spectra
Lunar reflectance
Solar Irradiance
SRF file
SRF for each processed band
DER output
Final Outputs
• Lunar spectral irradiances for input observations in sensor spectral bands

## Slide 6: LSICS Gitlab

## Slide 7: LSICS Gitlab

## Slide 8: LSICS structure
$LSICS/
config.toml
static_config.toml
main.py
data/
src/
Source: LASP, Coddington 2023

## Slide 9: Some words on interfacing lunar reflectance models
Definition of a main class for the models

## Slide 10: Some words on interfacing lunar reflectance models
Definition of subclasses inheriting from the main model class
GIRO
SLIMM
LESSR
Function to read the LUTs / model parameters
Model computation

## Slide 11: Distribution and usage
Public access to the official release (“main” branch) for users
Creative Commons license
  CC BY–ND — attribution required, no code derivatives allowed
  avoids having a formal usage agreement
Digital markers and public signature key
  to ensure that output products have been generated by the official agreed version of LSICS
  implemented using JSON tokens

## Slide 12: Some tests and results - MSG/SEVIRI

## Slide 13: Some tests and results - MSG/SEVIRI

## Slide 14: Switching lunar model / Inter-operability

## Slide 15: Future work
Complement the system with a series of functionalities that were identified while developing (e.g. adding WGS84 to J2000 + ITRF93, consolidating the data and the run traceability, etc.)
Complete work on the definition of a benchmark + testing
  Validation against the original lunar model implemented in the DR module
  New enhancements implemented in LSICS (such the process for checking the versions in the runs by users)
Formal documentation
  Functional requirements, code structure, file and data formats (I/O, SRF and internal/intermediate files), module interfaces (Interface Control Document)
  Lunar model functional description
  Documenting the system validation
Development of a toolbox to display the LSICS intermediate + final output, and extract relevant information such the run history ( traceability)
Release of version 1.0

## Slide 16
Thank you!
Questions are welcome.