## Slide 1: `
An Overview of The Arctic Observing Mission (AOM)
Ray Nassar1, Alec Casey1, John Evans2, Dan-Tam Nguyen2, Matt Arkett1, Chris Sioris1, Chris McLinden1, Joseph Mendonca1, Josep Aparicio1, Shen-En Qian2, Isabelle Jean2, Mary-Anne Fobert3, Alexander Trishchenko3 1) Environment and Climate Change Canada (ECCC)
2) Canadian Space Agency (CSA)
3) Natural Resources Canada (NRCan)
GSICS Annual Meeting
Mini-Conference: Highlights from Canada
March 23, 2026

## Slide 2: The Changing Arctic
Arctic temperatures have increased 3-4 times global average and this trend is expected to continue
Changes occurring in multiple Arctic systems (land, atmosphere, ocean, cryosphere) are linked to climate and other anthropogenic drivers
New, enhanced observations are needed over the Northern high latitudes to improve weather prediction, situational awareness and environmental science and monitoring for societal benefit
Permafrost Carbon
Weather & Climate
Resource Extraction
Climate Feedbacks
Hanaček et al. 2022, Ecological Economics
Schuur et al. 2015, Nature
Rantanen et al. 2022, Comm. Earth & Env.

## Slide 3: Satellite Orbits
Geostationary Orbit (GEO) gives rapid revisit, but satellite coverage is limited to ~60ºS-60ºN due to viewing geometry from equatorial orbit
Low Earth Orbit (LEO) satellites give global coverage but with low temporal revisit rates
A Highly Elliptical Orbit (HEO) can address the spatial/temporal gap over one circumpolar region, here the North

## Slide 4
Observations north of ~40°N
Proposed Canadian-led international satellite mission to provide improved environmental monitoring and situational awareness in the Arctic region
AOM

## Slide 5: AOM Orbit
Three Apogee (TAP)
Orbit
Many science and technical implementation factors considered & weighed in orbit selection process.
Three-Apogee (TAP) orbit selected to optimize apogee height (SNR and spatial resolution performance) while meeting geographic coverage requirements (for continuous meteorological observations down to at least 65°N).
Ground stations in both North America and Europe are required to enable continuous access to the AOM spacecraft throughout their operational period (apogee±1/3 orbital period).
Eccentricity | Apogee Height | Inclination | Period
0.50 | 41,885 km | 63.435° | 16 hours

## Slide 6: Proposed AOM Payloads and Partnerships
Space Weather Payload
Auroral Imager, Particle Detectors, Magnetometer
Varying levels of potential partnership are under discussion
Infrared Sounder
Meteorological Imager
Multi-spectral VIS-IR Imager (16+ bands - e.g. FCI, GXI, Canadian MSI)
Imaging Fourier Transform Spectrometer (IFTS)
6 hyperspectral bands:
NIR and 3 SWIR for retrieval of CO2, CH4, CO and solar induced fluorescence (SIF)
MWIR and LWIR for enhanced vertical information (temperature, water vapour, ozone, 3D winds) and other trace gas profiles for meteorology, air quality and climate.

## Slide 7: Imaging Fourier Transform Spectrometer (IFTS)
If observing mainly clear sky areas using a cloud mask from the Met imager, the IFTS can obtain hourly column-averaged CO2, CH4 and CO observations and solar induced fluorescence (SIF) observations over cloud-free land north of 40°N during daylight. CO2 and CH4 will be assimilated in a model to obtain surface fluxes.
Pixel size (km)
*Only binned pixels meet threshold precision & accuracy
Expected precision (1s) for binned pixel | 
XCO2 | ~2 ppm (~0.5%)
XCH4 | ~18 ppb (~1.0%)
XCO | ~ 5 %
SIF | ~1.5 Wm-2 sr-1 mm-1
Band | Wavelength (mm) | Wavenumber (cm-1) | SNR Goal & Threshold | Expected SNR
1) O2 A | 0.758 – 0.772 | 12953–13192 | 54 / 18 | 20
2) CO2 – 1 | 1.598 – 1.618 | 6180–6258 | 119 / 40 | 91
3) CO2 – 2 | 2.042 – 2.079 | 4810–4897 | 116 / 40 | 99
4) CH4, CO | 2.301 – 2.380 | 4195–4345 | 140 / 50 | 87
Baseline spectral sampling interval 0.30 cm-1
 | Binned Pixel | Unbinned Pixel
At 40,000 km | 3.6 km | 1.2 km
TAP orbit average | ~ 3.0 km | ~ 1.0 km
Using 2D focal plane arrays (FPAs), IFTS will record interferograms in a 128x128 (binned) pixel field-of-view (FOV) every 60 seconds.
54 FOVs observed per hour (due to repointing time).
Level 1
Level 2
Each binned pixel is made up of 9 ‘unbinned’ pixels, which can potentially be available for applications that favour spatial resolution over precision (if pointing stability goal can be achieved).
Due to changing satellite altitude, pixel size varies during orbit.
TAP
Tundra
Level 3
Hourly 3D CO2 and CH4 fields (1°x1°)
Level 4
Monthly CO2 and CH4 surface fluxes (1°x1°)
Level 0 Interferograms, later transformed to spectra
IFTS+
Possible addition of longwave and mid-wave infrared bands (LWIR, MWIR) would also enable measurements of N2O along with vertical profiles of CO2, CH4 and CO during day/night, summer/winter and over land/water.

## Slide 8: IFTS+ HEO IR Sounder
Imaging Fourier Transform Spectrometer (IFTS)
Band | Wavelength (mm) | Wavenumber (cm-1)
1) O2 A | 0.758 – 0.772 | 12,953 – 13.192
2) CO2 – 1 | 1.598 – 1.618 | 6180 – 6258
3) CO2 – 2 | 2.042 – 2.079 | 4810 – 4897
4) CH4 & CO | 2.301 – 2.380 | 4195 - 4345
5) LWIR | ~7.1 - 14.7 (goal) | ~680 - 1400 (goal)
6) MWIR | ~4.44 - 6.25 (goal) | ~1600 - 2250 (goal)
Baseline 20 cm aperture. Dual interferometer design adds ~50 kg, no added volume compared with 4-band IFTS. Each beamsplitter is optimized for its spectral region so SNR for NIR-SWIR is maintained. Interferometers can operate at different spectral sampling/resolution. Spacious 2nd level has room for 5th and 6th band (MWIR+ LWIR) delivering the most benefits.
5-band dual-interferometer IFTS
IFTS+ adds 2 new spectral bands (LWIR & MWIR) for vertical info on temperature, water vapour and 3D winds for meteorology, along with retrieval of trace gas profiles (O3, NH3, N2O, CO, CO2, CH4...).
Alternate scan patterns to intelligent pointing are now being studied at ECCC to optimize coverage for meteorological applications.
“Resizing” IFTS: e.g. 0.625 cm-1 spectral sampling to match IRS, GIIRS, GXS and Himawari Sounder; 160x160 pixels to improve instantaneous coverage and revisit, optical design changes to improve SNR / reduce dwell time.

## Slide 9: Studies on IR Sounder Scanning, Coverage and Revisit
From apogee ~116 Fields of View (160x160) are needed for circumpolar coverage north of 45°N and the rest of Canada, with view zenith angles ≤60°.
About one third of the time, dual satellite viewing is possible, giving ~105 FOVs/satellite, improving the revisit rate.
One satellite at apogee
Two satellite viewing
IFTS design changes to reduce dwell time from 60 s to ~20-23 s would enable ≤ 40 min. revisit

## Slide 10: VIS-IR Imager
Channel | Colloquial Name | Applications | Central λ (µm) | λ width (µm) | Resolution (km)*
VIS 0.4 | Blue | clouds, aerosol, surface | 0.444 | 0.06 | 1.0
VIS 0.5 | Green | clouds, aerosol, vegetation | 0.510 | 0.04 | 1.0
VIS 0.6 | Red | clouds & fog, snow/ice, winds | 0.640 | 0.05 | 1.0
VIS 0.8 | Veggie | vegetation, winds | 0.865 | 0.05 | 1.0
VIS 0.9 | Low-Level WV | water vapour (WV) | 0.914 | 0.02 | 1.0
NIR 1.3 | Cirrus | Cirrus detection | 1.38 | 0.03 | 1.0
NIR 1.6 | Snow/Ice | cloud phase, snow/ice | 1.61 | 0.05 | 1.0
NIR 2.2 | Particle Size | particle size, cloud phase, smoke | 2.25 | 0.05 | 1.0
IR 3.8 | Fire | fires, microphysics, winds | 3.80 | 0.40 | 2.0
WV 6.3 | Upper-Level WV | WV, winds, rainfall | 6.30 | 1.00 | 2.0
WV 7.3 | Lower-level WV | WV, winds | 7.35 | 0.50 | 2.0
IR 8.7 | Cloud-Top Phase | cloud phase, TPW | 8.70 | 0.40 | 2.0
IR 9.7 | Ozone | turbulence, total O3 | 9.66 | 0.30 | 2.0
IR 10.5 | Clean IR | SST, clouds temp | 10.50 | 0.70 | 2.0
IR 12.3 | Dirty IR | TPW, dust, ash | 12.30 | 0.50 | 2.0
IR 13.3 | CO2 | air temp, cloud height | 13.30 | 0.60 | 2.0
Each AOM satellite will carry a meteorological imager with 16 or more image channels.
View from the TAP Orbit’s North American Apogee:
*Resolutions are for FCI in GEO, but AOM resolution will vary throughout its elliptical orbit. AOM resolution will be ~17% coarser near apogee of the proposed TAP orbit, but will be finer than above when AOM is acquiring imagery at altitudes lower than GEO (35,786 km; AOM will be at GEO altitude at ±3.3 h from apogee).
The hyperspectral LWIR and MWIR band of the IR Sounder also provide observations of significant meteorological value, specifically temperature and humidity data with much more vertical information than from a VIS-IR imager, and possibly 3D winds. Assimilation of LWIR and MWIR radiances and 3D winds in NWP are expected to substantially improve forecast skill in northern regions.
Near real-time Level 1 imagery can be used directly by meteorologists to improve short-range forecasts and can be assimilated in numerical weather prediction (NWP) systems.
A wide range of Level 2 data products can also be retrieved including: aerosol, cloud, wind, rain, snow, surface albedo, skin temperature, fire hotspot, and sea/lake ice parameters.
FCI Instrument:

## Slide 11: Key Meteorological Benefits
Transformative data sets for nowcasting operations:
Increased temporal (≤ 15 mins) and spatial resolution (~1 to 2 km at nadir) over the pan-Arctic domain
Reduction of parallax effects at mid to high latitudes
Significant gains will be made in the IR channels (e.g. cloud top temperature)
Enhanced observations of:
  Wildland fires and smoke ▪ Tracking of high Arctic systems
  Blowing snow/blizzards ▪ More details and tracking of polar lows
  Thunderstorm activity ▪ Continuous ice motion (in cloud free areas)
  Sea spray and better observations for marine regions
Support METAREAs, VAAC, Aviation & Defence services etc.
Address capability gaps
Substantial contributions to NWP skill anticipated
Improved coverage of atmospheric motion vectors, particularly from 50-70 N (between dense GEO and LEO coverage)
Continuous radiance observations at pan-Arctic scale
LWIR and MWIR bands on GHG instrument will complement coverage of planned GEO IR sounders, with possibility for 3D wind products if sufficiently short revisit time can be achieved
TOA modeled radiative fluxes (24-h @ 15 min) at 30 km spatial resolution.
Daytime images Nighttime images
Red – 1.6 mm Greyscale - 11 mm
Green – 0.85 mm
Blue – 0.63 mm
Earth view from TAP orbit

## Slide 12: Space Weather Instrument Suite
HEO provides a unique vantage point for both in situ and remote sensing of space weather.
Space weather is outside of ECCC’s mandate, but of interest to OGDs: especially NRCan and DND.
AOM space weather instrument suite is less mature than other payloads, but could consist of:
  an Auroral Imager observing in the far-UV
  a magnetometer on a 1-2 m boom
  an energetic particle (electron, proton, ion) detector
  plasma analyzers
e.g. Auroral imaging from the past NASA Image mission

## Slide 13: AOM Timeline
2022-2025: Pre-formulation Studies – Phase 0
2025-2026: Working to secure funding for mission development and implementation as well as support from international partners.
Letters of Support from: EUMETSAT, FMI, NordMet Council, CEOS, WMO, …
If successful:
2028-2033: Phases A-C (Definition and Design)
2033-2038: Phase D (Build, integrate, launch, commissioning)
2038-2048: Phase E (Operations)
Notes: Select Phase 0 deliverables:
GHG instrument sub-orbital demonstration stratospheric balloon flight: August 2022
NOAA-funded meteorological imager adaptation study with L3Harris: Completed December 2022
Socio-economic benefits study (EuroConsult): Completed June 2023
GHG observing strategy (intelligent pointing) manuscript: Published October 2023
AOM CO2/NO2 science study (Univ. of Toronto): Completed March 2024
AOM Mission Design Contract (MDA, ABB, Airbus): Completed March 2025
GHG instrument Focal Plane Array (FPA) study: Started Fall 2023, ongoing
Various other science/application studies (AOM OSSE, orbit studies, etc): in progress

## Slide 14: Anticipated Benefits
Obtaining high density and high frequency observations of weather, climate, air quality and space weather over northern latitudes would benefit Arctic and northern communities in many profound ways, including:
Improved
Weather
Forecasting
Infrastructure
& Transport
Networks
Hazard Identification & Response
Climate Change Adaptation
& Resilience
Reducing GHG
Emissions
Arctic Environmental Stewardship

## Slide 15: International Perspectives
AOM could contribute to many international priorities including:
AOM could provide complementarity with many international missions:
  Extend the GEO ring to high northern latitudes (MTG/M4G, GeoXO, etc)
  Contribute to the CEOS Atmospheric Composition Virtual Constellation (AC-VC)
International partnership remains essential for AOM’s business case and to ensure overall mission success
Global Greenhouse Gas Watch (G3W)
Notes: Also note:
- WMO Vision for WIGOS in 2040
- Complementarity with other Canadian missions (RADARSAT+, WildFireSat, HAWC on AOS, TSMM)

## Slide 16: Summary
AOM is a high-priority initiative that Canada continues to advance​ with input from key international partners
AOM responds to ECCC, Government of Canada, and international priorities in the domains of meteorology, climate, air quality and space weather
AOM would deliver new observational capacity across these domains at unprecedented frequency over Canada and other Northern regions (above ~40° N)
Attending GSICS to learn more about this group and prepare for future participation.
Notes: Improve operations and service delivery in areas of weather, climate, air quality, and space weather
Collect authoritative data on greenhouse gases over northern latitudes to inform decision-making and support policies around climate change adaptation, mitigation and resilience
Improve the quality of life for Arctic and Northern communities
Enhance Canada’s contributions to Arctic monitoring and the international pool of satellite data

## Slide 18: AOM IFTS Calibration Sub-system
Open: For observations or for Lunar calibration
Diffuser 1: Primary solar diffuser for Solar calibration
Diffuser 2: Secondary solar diffuser for Solar calibration and tracking degradation of Diffuser 1
Diffuser 3 (reflective): would work with onboard LED calibration sources
Blackbody & shutter: For calibration of LWIR/MWIR bands, acts as a shutter for other bands

## Slide 19: IFTS Onboard Calibration Light Source
At least 4 LEDs needed for 4 NIR-SWIR bands, but some redundancy would better enable detection of degradation to onboard sources.
Potential topic for technology development prior to Phase B

## Slide 20: VIS-IR Imager: Coverage
AOM Mission requirements stipulate that the VIS-IR imager provide full disc imagery every 15 minutes or less, with continuous coverage above 65N and a goal for regional/mesoscale scan capability
Figures illustrate the % of time in a 48-hour ground track repeat period that a given location can be imaged by the VIS-IR Imager with acceptable viewing geometry (View Zenith Angle < 70°)