## Slide 1: Vision for GSICS-led Advances in Lunar Calibration
Tom Stone (USGS) — Presenter
The LSICS Development Team
  Sébastien Wagner (EUMETSAT)
  Matthijs Krijger (Earth Space Solutions)
  Hugh Kieffer (Celestial Reasonings)
  Masaya Takahashi (JMA)
  Stefan Adriaensen (VITO)
  Javier Gatón Herguedas (Univ. Valladolid)

## Slide 2: Focus Areas for Directed Efforts, 5−10 Years
Addressing GSICS objectives
Engagement with New Space entities
Developing the Lunar Spectral Irradiance Calibration System (LSICS)
Documenting Best Practices for deriving and applying lunar calibration
Evaluating and propagating uncertainties
Developing other lunar models
Exploiting and promoting the capabilities of lunar calibration
Acquiring new fiducial reference measurements
Data preservation and access
Applying machine learning techniques
Communicating lunar calibration requirements to mission developers
Promoting a distribution of labor — community-wide contributions

## Slide 3: Addressing GSICS Objectives
Efforts toward improving lunar calibration systems
Applying lunar calibration to achieve higher accuracy satellite data products
  Common objective among National Agencies, International Orgs and New Space entities
Improved lunar measurements from satellite instruments
  Being used for model development, e.g. SLIMM, LESSR (SCIA, GOME-2)
Finding a consensus lunar model
  The GSICS recommended lunar calibration reference
  Best absolute accuracy, determined by comparison to high-accuracy lunar measurements
    Dedicated projects: air-LUSI, ARCSTONE, other Agency efforts
  Periodic inter-comparisons and review of the selection

## Slide 4: Addressing GSICS Objectives
Developing lunar inter-calibration techniques
The Moon: a stable common reference
  Enables inter-consistent calibration across platforms
    Supports multi-satellite observatories (constellations)
      e.g. Landsat-Next
    Addresses recent trend toward fleets of small satellites
      many with no on-board calibration capability
  Enables back-calibration of historic datasets
    Toward developing long-term data records
Lunar models must be used to adjust for the different Moon observation geometries
  Current models fulfill this need with high relative precision

## Slide 5: Addressing GSICS Objectives
Increasing data-sharing by Agencies
Potential for use with lunar model development
Agency lunar observations often are internal calibration data → Restricted Access
Attempted solution (2014): the GSICS Lunar Observation Dataset (GLOD)
  Current efforts toward revision of the database — contributions and usage
  Involvement of the GSICS Data Working Group
Communicating developments with the GRWG IR and MW subgroups
Agreed: reporting on lunar calibration activities kept within the topical groups
  Maintain awareness by peers
Cross-communication of activities: coordinated by the Lunar Subgroup

## Slide 6: Engagement with New Space Entities
A Goal: convey the value of lunar cal beyond sensor radiometric performance
Improve EO data quality using lunar calibration
  Makes data products more attractive as potential procurements by Agencies (data buys)
Incentive for New Space entities to collaborate with GSICS
  Contribute to lunar calibration development efforts
New Space deployments of satellite fleets
Promoting the capabilities of the Moon as a common reference:
  inter-calibration of fleet sensors
  high-precision inter-consistency of data products
A win-win situation:
Higher data quality → a benefit to New Space entities
Improved lunar measurements → an asset for advancing satellite lunar cal

## Slide 7: Lunar Spectral Irradiance Calibration System (LSICS)
A framework for operating lunar irradiance models
Consistent pre- and post-processing around the DER models
    DER: Disk Equivalent Reflectance
  pre-processing: observation time and location → LOAS
    LOAS: Lunar Observation Angle Set; geometric angles of phase and libration
  post-processing: model-generated DER → spectral irradiance
    Filtering the solar spectrum, convolving the solar spectrum and sensor SRF
Inter-changeable core lunar models (DER)
Planned demonstration: 2nd lunar model inter-comparison exercise
A repository for lunar models
Intended to be archival — static records of previous models and versions
Access for registered users

## Slide 8: Documenting Best Practices
A living document
communal editing by the LSICS group, with accommodating alternate views
The need: reliable operational calibration against the Moon requires both:
  accurate lunar reference models and
  high-quality measurements from sensors
An example: commonly used relative trending applications require only consistent measurements
  Data processing routines have been developed quickly and automated
Lunar calibration can provide absolute calibration with <1% uncertainty
  Requires careful attention to irradiance measurements from images, e.g.:
    spatial response (pixel solid angle)
    spatial sampling and oversampling factor (possibly pixel-dependent)
High-accuracy routines can be implemented in in-line image processing

## Slide 9: Documenting Best Practices
A large, continually progressing task
Many aspects of lunar calibration to be documented:
  acquisition specifications — cadences, preferred phase angles, …
  impacts of off-nadir viewing — s/c thermal drift, scan mirror angle, …
  techniques for deriving lunar models
    data fitting procedures
    assessing the reference datasets
    evaluating model output uncertainties
  mission planning to accommodate Moon viewing, including end-of-life
  …
The intention: consolidate immediately applicable info
  for easy access
  for expedient reference by the community.

## Slide 10: Other Critical Tasks and Active Efforts
Tracking Uncertainties
In outputs from the lunar models (the calibration reference)
  tracing to the reference measurements used as the basis for models
In calibration measurements of the Moon taken by sensors
Developing Additional Models
Polarisation models
Expanding to other wavelength domains: thermal IR, microwave
Spatially resolved radiance models
Exploiting other uses for lunar images
Geometric calibration (instrument pointing)
Image quality evaluation, MTF

## Slide 11: Summary — Goals of the Vision
Conveying the impacts of a refined lunar calibration system
Providing high-precision inter-calibration for constellation-type observatories
Improved accuracy of absolute radiometric calibration on orbit, by reference to the Moon
Mutual benefits for Agencies and New Space derived from collaborations
Providing tools and guidance information for applying lunar calibration
toward exploiting the improvements and advantages of using the Moon

## Slide 12: Thank You !

## Slide 13: Backup Slides — Supplemental Notes and Descriptions
Addressing GSICS Objectives
all agencies can derive benefit from improved lunar calibration references and best practices
shared lunar measurements can lead to improved lunar calibration reference models
a consensus lunar model can and should be a GSICS goal
develop inter-calibration algorithms using the Moon as a transfer target
increase interaction with IR and MW subgroups
Engagement with New Space Entities
message: improved lunar calibration can make commercial EO datasets more valuable to satellite operating agencies, and therefore more attractive as potential procurements by the agencies. This can and should create an incentive for New Space to collaborate with and contribute to GSICS lunar calibration efforts, toward improving the radiometric quality of their EO data products and lunar measurements.
New Space entities are operating fleets of small satellites – lunar calibration can provide high-precision inter-consistency among the fleet components

## Slide 14: Backup Slides — Supplemental Notes and Descriptions
LSICS development
a framework for operating lunar models in a controlled environment
adding lunar disc equivalent reflectance (DER) models, and selecting the default
evolution of the GSICS standard lunar reference
documenting and disseminating information on the usage and accuracy of LSICS
Documenting best practices for developing and applying lunar calibration
deriving irradiance measurements from sensor images
acquisition strategies: preferred phase angles, cadence of Moon observations, …
potential effects of off-nadir viewing
provide guidance and recommendations on pre-launch characterisations for lunar obs
analysis techniques for lunar model development
Evaluating uncertainties
uncertainties in irradiances derived from EO satellite imager observations
uncertainties in model outputs
propagation and combination all through the calibration process

## Slide 15: Backup Slides — Supplemental Notes and Descriptions
Additional model development
polarisation models
extended wavelength ranges: UV, thermal IR, microwave
spatially resolved lunar radiance models
Exploiting and promoting additional capabilities
the advantages of an extra-terrestrial stable reference, impacts of improved accuracy
cross-calibration and back-calibration: harmonising EO measurements across platforms and over time, toward building inter-consistent long-term data records
transfer of pre-launch calibration to on-orbit operations
bridging a gap in otherwise continuous observation records
Acquiring new fiducial reference measurements
assessing needs and desired characteristics: spectral resolution, SI traceability, …
current efforts for acquisition: air-LUSI, ARCSTONE, other agency projects
requiring stated uncertainties — traceable evaluation and error propagation
fostering further collaboration between agencies and New Space partners

## Slide 16: Backup Slides — Supplemental Notes and Descriptions
Data preservation and access
particularly for reference measurements used for lunar modeling
space-based EO instruments — typically calibration data, thus generally not available
potentially reforming the GSICS Lunar Observation Database (GLOD)
coordinating with the GDWG
Applying machine learning techniques
goal: a parametric form for predicting lunar disk equivalent reflectance (DER) given an input observation geometry angle set (phase and librations)
merging large datasets, e.g. from lunar orbiters, for building up a basis for modeling
Communicating lunar calibration requirements to mission developers
early in the mission design process, to ensure the capability to view the Moon
the need for a liaison to present lunar calibration advantages and promote its use
Promoting a distribution of labor — community-wide contributions
improved lunar calibration can benefit the whole community
contributors to become stakeholders