## Slide 1: Towards (Aerosol) Retrieval Consistency and Continuity across 2 MODIS + 3 VIIRS
Robert C. Levy. (NASA Goddard Space Flight Center)
Virginia Sawyer (STC/GSFC)
Mijin Kim (Morgan State/GSFC)
Yingxi Shi (UMBC/GSFC)
2026
Acknowledgements:
MODAPS team at GSFC (MODIS processing)
A-SIPS team at U. Wisconsin (VIIRS processing)
https://darktarget.gsfc.nasa.gov

## Slide 2: Why do we care about aerosols?
They affect visibility
They affect human health and morbidity
They enable clouds and precipitation
They have roles in Earth’s chemistry (carbon, sulfate, etc)
They have roles in biology (e.g. transport nutrients)
They directly and indirectly impact the radiative budget
They are both natural and manmade
They are inhomogeneous in space and time
Their distributions are changing
The science of aerosols is truly “interdisciplinary”
We need datasets that characterize climatology, trends and variability

## Slide 3: Why do we care about aerosols? (Bonus)
They affect visibility
They affect human health and morbidity
They enable clouds and precipitation
They have roles in Earth’s chemistry (carbon, sulfate, etc)
They have roles in biology (e.g. transport nutrients)
They directly and indirectly impact the radiative budget
They are both natural and manmade
They are inhomogeneous in space and time
Their distributions are changing
The science of aerosols is truly “interdisciplinary”
We need datasets that characterize climatology, trends and variability
Their “retrieval” helps fine-tune VIS/NIR imager calibration!!!

## Slide 4: Dark Target (DT) Aerosol retrieval Algorithm
May 4, 2001; 13:25 UTC
Level 1 “reflectance”
What a sensor observes
OCEAN
GLINT
LAND
May 4, 2001; 13:25 UTC
Level 2 “product”
AOD
1.0
0.0
Attributed to aerosol (AOD)
Established by Kaufman, Tanré, Remer, et al (1997)
Modified by Remer, Levy, Gupta, Sawyer, Shi et al (2005, 2010, 2013, 2015, 2020, etc.)
DT
Requires: Observations of spectral reflectance in 7 selected bands between ”blue” and “SWIR” wavelengths (other bands help with cloud/surface masking and filtering)
Retrieves: AOD at 0.55 mm, spectral AOD (AE), cloud-cleared reflectances, diagnostics, Quality Assurance and Confidence
Notes: Note that now there are many more algorithms for MODIS, including Deep Blue (retrieves over bright surfaces using a 0.412 micron channel that land surface is much darker), Also MAIAC, which uses multi-day observations to separate quickly changing aerosols from slowly changing land surfaces

## Slide 5: 20+ years of MODIS: Terra vs Aqua time series (with C6.1)
With same Collection 6.1 algorithm, no visual difference between Terra and Aqua globes
Time series indicates Terra offset high compared to Aqua by about 0.015 (10-15%).
Yet, both within expected uncertainties
Small calibration adjustments of 2% or less might help, but requires doing all wavelength bands and maybe also time-dependence
Aqua
Terra
AOD: May 2023

## Slide 6: MODIS Collections
https://atmosphere-imager.gsfc.nasa.gov/collections/overview
C001: Initial algorithms at Terra launch
C003: Provisional for both Terra and Aqua
C004: First significant “validation” (2003)
C005: First real “science” (2005)
C051: Some calibration and bug fix (2008)
C006: Major upgrades to science (2013)
C061: updates to the L1B. (2017)
C007: L1B, Science, formats!: MID 2026!
2000 2003 2006 2009 2012 2015 2018 2021
Towards “Collection 7” (C007)
  Level 2: Modernize to NetCDF Climate and Forecast file format and metadata conventions
  Updated L1B calibration/geolocation. Possibly include a polarization correction
  Level 3: TBD, but will look much as does now (e.g. 1° x 1° grids at daily, 8 day and monthly).
  Science updates: 1) Ocean nonspherical dust, 2) improved cloud mask, 3) heavy aerosol coverage.
“legacy” as MODIS missions (both Terra and Aqua) will end sometime soon)
  How does orbital drifting (since 2022) impact long term record (e.g., sampling of clouds, high latitudes, sun angles, etc.) ?

## Slide 7
Global Climate Observing System (GCOS)
requirements for Aerosol Optical Depth (AOD) climate data record (CDR):
Target metric | Target
Horizontal Resolution | 5-10 km, globally
Accuracy | MAX(0.03 or 10%)
Stability / bias | <0.01 / decade
Time Length | 30+ years
Temporal Resolution | 4 h
EXTEND with VIIRS
EXPAND with GEO and other platforms
  }
  }
  }
MODIS data record
Focus on VIIRS today

## Slide 8: Extend record with VIIRS (Visible-Near Infrared Radiometer Suite)
VIIRS on Suomi-NPP (c. 2011)
MODIS on Aqua (c. 2002)
With MODIS ending before 30 years, we need continuity provided by similar instrument = VIIRS. Ported DT algorithm from MODIS to VIIRS
Suomi-NPP, NOAA20 and NOAA21 are in orbit. VIIRS V2.0 products agree with MODIS C6.1 to ±0.02 in AOD units.
Additional VIIRS sensors to launch NOAA’s JPSS3/4 into at least the late 2030s, thus satisfying the multi-decadal needs of GCOS.
2000  MODIS  2026
2011  VIIRS  2030+
March 2015
Sawyer et al., 2025 (VIIRS V2.0)

## Slide 9
Slope of the linear regression where p ≤ 0.01.
Some places, the 10-year trends may be different than 20-year trends (of MODIS).
Overall, SNPP sees the same world as Terra / Aqua (except for southern midlatitude ocean?)
Consistency of Dark Target AOD 11-Year Trends (SNPP vs Aqua):
MODIS-Aqua
VIIRS-SNPP
2012-2023
Sawyer et al., 2025 (VIIRS V2.0)

## Slide 10: Regional trends (picking some 10° x 10° boxes)
Wildfires in western Canada drive variability. Autumn/winter flat.
Reductions seen in Eastern U.S. due to policy regarding emissions. But no trend during SNPP lifetime. Spike in 2021 due to fires
Coherent interannual change in eastern China, strong decrease during SNPP period.
Sawyer et al., 2025 (VIIRS V2.0)

## Slide 11: MODIS C6.1 vs VIIRS 2.0
Overall tendencies are consistent.
All AODs within ± 0.02-is to MODIS-Aqua but....
SNPP > Terra > Aqua > N20
And total range of ±0.05
0.22 vs 0.17 “not insignificant” for understanding climate
Can we do better?

## Slide 12: MODIS C6.1  C7 : VIIRS V2.0  V2.1  V2.2 Algorithm improvements common to both streams
High-resolution 3x3 red-band cloud masking over ocean (250 m for MODIS, 375 I-band for VIIRS)
Log-fit to lookup table when AOD < 0.2 (disallows negative AOD)
Detect (and retrieve) dust using non-spherical model over ocean
Update formulas for Surface Reflectance Parameterization (SRP) over land that estimates Blue, Red & SWIR2.½ bands via NDVI, Urban Percentage & Angles. Now same formulas for both.
Uses same “ancillary” GEOS-IT meteorological re-analyses.
Same ”Yori” (University of Wisconsin) aggregation for Level 3 product
Bug fixes as needed

## Slide 13: MODIS C6.1  C7 : VIIRS V2.0  V2.1  V2.2 Algorithm updates that are separate
MODIS C6.1  C7 (MxD04_L2)
Products are in NetCDF4 (to match VIIRS)
DT-only SDS names, groups, and metadata are simplified (to match VIIRS)
Reads in “entire” granule for cloud and other masking (to match VIIRS)
New “call back” to retrieve heavy surface-level aerosol over eastern Asia
C7 L1B files include “solar eclipse flag”
Uses C7 Wisconsin Cloud mask (3 tests for clouds + other tests for Dust Detection
Deep Blue (DB) retrievals and DB/DT “merge” remain in same MxD04_L2 file
VIIRS V2.0  V2.1  V2.2 (AERDT_L2)
SDS names exactly match MODIS C7
Does not need a call-back to retrieve heavy surface-level aerosol over Asia
Uses updated Wisconsin Continuity Cloud Mask
Fixes QA-Filtering bugIntroduces X-calibration between V2.0 and V2.1.
Deep Blue (DB) retrievals remain in separate file (AERDB) and no DT/DB merge provided by the aerosol teams.

## Slide 14: Overall “Algorithm Updates”
C6.1
C7
nearly unchanged distribution
High outliers reduced
MODIS: April 2005

## Slide 15: X-calibration Coefficients in DT algorithm (MODIS-Aqua  VIIRS). Not applied to MODIS
Band Pair [nm] |  |  |  | X-calibration Coefficient [1] Lyapustin et al. (2023), [2] Meyer et al. (2020), [3] Wang et al. (AGU 2024) |  |  |  | 
 |  |  |  | [1] | [2] | [1] | [2] | [3]
VIIRS |  | MODIS |  | AQUA/SNPP | AQUA/SNPP | AQUA/N20 | AQUA/N20 | AQUA/N21
M3 | 478 - 488 | B3 | 459 – 479 | 0.98 | - | 1.03 | - | 1.06
M4 | 545 - 565 | B4 | 545 – 565 | 0.98 | - | 1.04 | - | 1.08
M5 | 662 - 682 | B1 | 620 – 670 | 0.98 | 0.95 | 1.02 | 1.00 | 1.02
M7 | 846 - 885 | B2 | 841 – 876 | 0.97 | 0.97 | 1.01 | 1.01 | 1.02
M8 | 1230 - 1250 | B5 | 1230 – 1250 | - | 0.99 | - | 1.02 | 1.04
M10 | 1580 - 1640 | B6 | 1628 – 1652 | - | 0.98 | - | 1.02 | 1.07
M11 | 2225 - 2275 | B7 | 2105 – 2155 | - | 0.97 | - | 0.99 | 1.00
Courtesy Mijin Kim

## Slide 16: VIIRS DT AOD Changes : V2.2 vs V2.1 vs V2.0
Key Changes in V2.1: X-cal, SRP over land
- Decreased SNPP over land
- Increased NOAA-20 everywhere
V2.2: Log-fit, Coastal retrieval
- Increased near-zero AOD over land
V2.1 – V2.0
V2.2 – V2.1
V2.2
Courtesy Mijin Kim

## Slide 17: X-Cal applied reduces overall bias
V2.0 N20-SNPP (Before X-calibration)
Overall offsets much closer to zero!
Differences are primarily due to cloud positions?
Courtesy Mijin Kim
V2.1 N20-SNPP (After X-calibration)

## Slide 18: Changes in VIIRS vs. MODIS Aqua (C6.1) relationship before and after Terra drift
Land 0.026, Ocean 0.008
Land 0.018, Ocean 0.001
V2.1 vs Aqua C6.1: November 2019 (before Aqua drift)
Courtesy Mijin Kim
Land 0.029, Ocean 0.021
Land 0.023, Ocean 0.016
V2.1 vs Aqua C6.1: November 2025 (1.5 hours apart!)

## Slide 19: MODIS C7: ”Tier 1” (2008-2018) and three VIIRS V2.2 LAND

## Slide 20: MODIS C7: ”Tier 1” (2008-2018) and three VIIRS V2.2 OCEAN

## Slide 21: MODIS C7 vs VIIRS 2.2
Overall tendencies are even more consistent!
All AODs within ± 0.01-ish!
We are doing much better!!!
Note, no X-Cal applied to MODIS-Terra

## Slide 22
Dark Target (DT) Aerosol Retrieval Project
One algorithm + many sensors = All daylight globe
https://ladsweb.modaps.eosdis.nasa.gov/missions-and-measurements/applications/geoleo/
https://darktarget.gsfc.nasa.gov