## Slide 1: The Lunar Irradiance Model of ESA (LIME)
C. Toledano (UVa), S. Adriaensen (VITO), A. Bialek (NPL), Á. Barreto (AEMET), R. González (UVa), P. De Vis (NPL) , J. Gatón (UVa) and M. Bouvet (ESA)
GSICS Annual and Executive Panel meeting, 23-27 March 2026, Ottawa, Canada.

## Slide 2: Outline
LIME latest advancements
Toolbox
Polarisation
Next steps

## Slide 3: LIME model approach
Strategy:
  Irradiance measurements
  SI traceable (NPL calibration)
  Langley plot method for atmospheric correction
  Include polarisation
Objective: 2% uncertainty (k=2)
Fit to ROLO equations for lunar reflectance
Lunar Irradiance Model of ESA
SI: International System of units

## Slide 4: Instrument
Cimel CE-318TP, standard in AERONET
9 filters 440-1640nm
Modifications - Bands: 440, 500, 550, 675, 780, 870, 935, 1020, 1640 nm
  Direct Moon polarization measurements

## Slide 5: Langley plot method: TOA lunar irradiance
m=1
m=2
m=5
TOA signals
TOA signal x calibration = TOA irradiance

## Slide 6: Sites
Since March 2018 (>600 nights)
Izaña Observatory (2400 m)
Toledano et al., ACP, 2018
Cuevas et al., ACP, 2022
Teide Peak Obs. (3555m a.s.l.)
Izaña Obs. (2400m a.s.l.)

## Slide 7: Model fitting
Irradiance (Wvm-2nm-1)
Relative difference
Phase angle (degrees)

## Slide 8: Model fitting
Residuals model-observations
Phase angle (degrees)
Relative difference (Irradiance)

## Slide 10: Comparisons
Comparison of LIME vs. Proba-V

## Slide 11: Comparisons
Comparison of LIME vs. Proba-V

## Slide 12: (Hyper)spectral reflectance
6 lunar cycles at Izaña
  2022 (Apr, May, Jun, Sep)
  2025 (Jun, Oct)
SOLYS2 tracker
ASD spectrometer

## Slide 13: (Hyper)spectral reflectance
ASD measurements were taken over 6-month campaign in 2022 and 2025
Measurements in absorption features are too noisy and are omitted (replaced using spectral interpolation)
Data divided in bins of 10° spanning -95° to 95° (Fig A)
Dependence of spectral shape with phase angle (Fig B)
linearly interpolated with phase angle to phase angle required within the LIME-TBX (Fig C)
(A)
(B)
(C)
Dataset available on Zenodo
https://doi.org/10.5281/zenodo.10534235

## Slide 14: (Hyper)spectral reflectance
LIME MODEL: set of coefficients (from fitting to ground-based Lunar measurements)
+
curves for spectral interpolation (from hyperspectral Lunar measurements)
+
uncertainty estimates
Absolute irradiance
High spectral resolution

## Slide 15: Latest updates
LIME coefficients computed with Cimel data until Nov. 2025.
ASD curves improved and updated.
  New masking algorithm has been developed to remove outliers
  New ASD dataset (new masking and data from 2025) provided to LIME-TBX and on Zenodo
  New ASD data consistent with 2022 data within the uncertainties, but removes spectral artefacts.

## Slide 16: LIME Toolbox
Simulates:
  Irradiance
  Integrated Irradiance (Signal)
  Reflectance
  Degree of linear polarisation

## Slide 17: LIME Toolbox
Input:
  Geographic coordinates & datetime/s
  Selenographic coordinates
  Satellite name & datetime/s
    User may add satellites if they have .tle or .osf files.
  Optional: SRF file in GLOD format

## Slide 18: Latest updates
LIME coefficients computed with Cimel data until Nov. 2025.
ASD curves improved and updated.
  New masking algorithm has been developed to remove outliers
  New ASD dataset (new masking and data from 2025) provided to LIME-TBX and on Zenodo
  New ASD data consistent with 2022 data within the uncertainties, but removes spectral artefacts.
Toolbox (applicator) updated
  New features (…)
  Version v1.4.1

## Slide 19: Polarisation
Cimel has 3 polarisers
0º, 60º, 120º
Degree of Linear Polarisation::
Li et al., 2009

## Slide 20: Polarisation
Polarisation (with sign):
Reference plane: Sun-Moon-observer >> calculation of Moon tilt angle.
Stokes vector (Cimel reference):
  I=2/3 (I0+I60+I120)
  Q=2/3 (2I0-I60-I120)
  U=-2/ √3 (I120-I60)
Rotation to the scattering plane:

## Slide 21: Polarisation
From Cimel data (500nm)

## Slide 22: Polarisation
Fit for each wavelength – 5th order polynomial

## Slide 23: Polarisation
Comparison to Lyot (1929)
-150
-120
-90
-60
-30

## Slide 24: Latest updates
LIME coefficients computed with Cimel data until Nov. 2025.
ASD curves improved and updated.
  New masking algorithm has been developed to remove outliers
  New ASD dataset (new masking and data from 2025) provided to LIME-TBX and on Zenodo
  New ASD data consistent with 2022 data within the uncertainties, but removes spectral artefacts.
Toolbox (applicator) updated
Polarisation model developed and included in the Toolbox

## Slide 25: Next steps
New ESA contract (start April 2026)
Objectives:
  Include new VIS and SWIR channels
  Improve polarization model
  Improve fitting
  Comparison to datasets
  Use LIME to derive aerosol optical Depth
  Support to users

## Slide 26: Next steps
  Include new VIS and SWIR channels:
26
440
500
675
870
1640
1020
1240
1550
2060
2130
550
780

## Slide 27: Summary
LIME model updated (inc. polarisation)
Toolbox available
Improvements ongoing
https://lime.uva.es
http://calvalportal.ceos.org/lime
GSICS Annual and Executive Panel meeting, 23-27 March 2026, Ottawa, Canada.

## Slide 28: Acknowledgments

## Slide 29: Thanks!