## Slide 1
TOWARD FIRST SPACEBORNE MULTI-FREQUENCY OBSERVATION OF SEA SURFACE SALINITY
EARLY IN-ORBIT PERFORMANCE OF MICAP L/C/K BAND INTERFEROMETRIC RADIOMETERS:
Hao LIU1， Jieying HE1
PAYLOAD TEAM
Donghao HAN1, Cheng ZHANG1, Lijie NIU1, Xing TONG1, Bingxu LI1,2, Huan MA1,2, Ji WU1
OCEAN SALINITY TEAM
Wenyu WANG1, Xiaolin TONG1, Zhou ZHANG1, Zhenzhan WANG1
SOIL MOISURE TEAM
Huizhen CUI1, Tianjie ZHAO3, Jingyao ZHENG3, Jiashuo GUO3,2
GROUND SEGMENT
Wu ZHOU4, Te WANG1, Ziquan LIU1

## Slide 2: OUTLINE
MICAP Instrument Description
Status During Commissioning Phase
Early In-orbit Performances
Early In-orbit SSS/SST/WS & Soil Moisture
Conclusion

## Slide 3: OUTLINE
MICAP Instrument Description
MICAP Instrument Status During Commissioning Phase
MICAP L/C/K Band Radiometers Early In-orbit Performances
MICAP Early In-orbit SSS/SST/WS & Soil Moisture
Conclusion

## Slide 4: Space-borne Salinity Missions in Last Decades
2D Interferometer
3-beam pushbroom
Conical scan

## Slide 5: MICAP INSTRUMENT OVERVIEW
Instrument Type: a suit of active/passive instrument package
  Passive part: L/C/K band one-dimensional MIR (microwave interferometric radiometer)
  Active Part: L-band DBF (digital beamforming) scatterometer
  Antenna: parabolic cylinder reflector antenna (~5.5*3m) with linear array feeds.
Motivation of the design
  1D MIR: balanced system complexity & performance
  Parabolic cylinder reflector & linear feed array: to include L-band DBF Scat for roughness correction, & C/K band MIRs for SST correction
  First Spaceborne…
  1D Synthetic Aperture Radiometer
  Multi-frequency Synthetic Aperture Radiometer
  DBF Scatterometer
  On-board RFI Detection & Mitigation for Synthetic Aperture Radiometer

## Slide 6
1.4GHz L-Rad
18.7GHz K-Rad
6.9GHz C-Rad
1.25GHz L-Scat
MICAP Instrument Architecture
Satellite Platform Subsystems

## Slide 7: MICAP Pre-launch Activities
RMS ≤ 0.2mm
  Reflector Assembly & Surface Accuracy Measurement
  Antenna Pattern Measurement in Cylindrical Near-Field
  L-Band
  C-Band
  Airborne Campaign
  On-board RFI Detection & Mitigation OFF/ON
  Anechoic Chamber Test
  Point Response
  NeDT
  TVAC Calibration
  Vraw vs. Tcal
  TL vs. Tph

## Slide 8: OUTLINE
MICAP Instrument Description
MICAP Instrument Status During Commissioning Phase
MICAP Early In-orbit Performances
MICAP Early In-orbit SSS/SST/WS & Soil Moisture
Conclusion

## Slide 9
Successful Launch of Chinese Ocean Salinity Satellite at Nov.14, 2024 !
Orbit type: sun-synchronous
Orbit altitude: 654km
Ascending/descending local times: 6:00 pm/am

## Slide 10: MICAP In-Orbit Health Monitoring
High Temperature Condition
Low Temperature Condition
  Reflector Temperature
The sensor-measured reflector surface temperature points are well within the pre-launch analysis range.
  SEU
SEU Mitigation: Dynamic Reconfiguration/Scrubbing
TA Counts after correction
TA Counts before correction
SEU Event
  Receiver Temperature
The thermal control stability of L/C/K-Rad Receivers is well within ±0.1℃

## Slide 11: MICAP L-Rad On-board RFI Thresh-hold Parameter Optimization
  STEP 1: On-board RFI Detection & Mitigation OFF
  STEP 2: Raw-data downlink mode, 10ms integrated, 13-subband × complex cross-correlations
  STEP 3: On-board RFI Detection Thresh-hold Optimization
  On-board Calibrated 10-ms, 13-Subband X-POL TA
  On-board Calibrated 10-ms, 13-Subband Y-POL TA
  On-board Calculated 10-ms, 13-Subband XY Cross-correlation Counts
  On-board Calculated 10-ms, 13-Subband X-POL Kurtosis
  On-board Calculated 10-ms, 13-Subband Y-POL Kurtosis
  STEP 4: Nominal Operational Mode (downlinking 1s-integrated, 13-subband data)
THP2.PE.6, TH4.P10.1

## Slide 12: OUTLINE
MICAP Instrument Description
MICAP Instrument Status During Commissioning Phase
MICAP L/C/K Radiometers Early In-orbit Performances
MICAP Early In-orbit SSS/SST/WS & Soil Moisture
Conclusion

## Slide 13: TA/TB Calibration & TB Reconstruction
First Multi-Frequency & One-dimensional Synthetic Aperture Radiometer In-Orbit
MICAP SIMULATOR

## Slide 14: TA Calibration (1): Internal Calibration
External Calibration is needed to mitigate the uncertainties of internal noise sources, including in-orbit drifts.
Periodical Internal Calibration
  Total Power Calibration: Internal Noise Source injection & Match Load
  Inter-channel Phase Calibration: Correlated Noise Source Injection
System Timing
  1 Second Cycle includes ten 100ms sub-cycles, one sub-cycle includes ten 10ms steps
  Cutting-off the first 1ms of each 10ms step to protect the receiver from scatterometer transmission
  Thanks to the excellent thermal control performance, 96 out of 100 steps are used for observation, only 4 steps for internal calibration
  Running average technics are used to reduce the calibration noise

## Slide 15: TA Calibration (2): Cold Sky Calibration
Cold Sky Calibration
  Using Cold Sky Observations to calibration the 12×2 internal noise diodes, whose noise temperature may differ from TVAC measurement on ground and exhibit drifting in early in-orbit stage
Satellite Cold Sky Maneuver
  Continuous maneuver, continuous observation
  Using Observations at which positions both antenna’s forward main beam and (majority of) backward beam are pointing to cold sky
X-pol TA(ch1-ch12) Before and After Cold Sky Calibration, comparing with Simulation
TB NeDT Evaluation Using Cold Sky Views
(＜0.1K)

## Slide 16: TB Calibration & Reconstruction
Manuel Martín-Neira, The Flat Target Transformation,
IEEE TGAS 2008
SMOS: Flat Target Transform (FTT) Approach
  Using Cold sky as reference target
MICAP: Sea Target Transform (STT) Approach
  Using dedicated ocean surface as reference target, the selection of which is strictly constrained with localization and ocean/atmosphere conditions
  Better scene similarity & scaling not needed
  Possible to implemented for 1D FOV
Differential TB Reconstruction for Interferometric Radiometers
  Reduce the contribution of receiver backward noises (Tr term)
  Minimize the uncertainty & non-consistency of element antenna patterns

## Slide 17
BT Recon. Without STT
Ocean Calibration
RMSE: 0.46K
BT Recon. With STT
RMSE:1.48K
Orbital Brightness Temperature
O-B
(Observation - Simulation)

## Slide 18
20250329 Tropical Cyclone Courtney
MICAP Observation
MICAP Simulation
L-band
C-band
K-band

## Slide 19
MICAP TB Map Comparing with SMAP & AMSR-2
MICAP L-Band X-pol
MICAP C-Band X-pol
SMAP L-Band H-pol
AMSR-2 C-Band H-pol
AMSR-2 K-Band H-pol
MICAP K-Band X-pol
20250220 Asc
20250220 Asc
20250220 Asc
20250220-20250222 Asc INC:33~40 EASE_GRID（15km）
20250220-20250222 Asc INC:33至40 EASE_GRID（15km）
20250220至20250222 Asc INC:33-40 EASE_GRID（15km）

## Slide 20
MICAP L-Band Y-pol
MICAP C-Band Y-pol
SMAP L-Band V-pol
AMSR-2 C-Band V-pol
AMSR-2 K-Band V-pol
MICAP K-Band Y-pol

## Slide 21: OUTLINE
MICAP Instrument Description
MICAP Instrument Status During Commissioning Phase
MICAP L/C/K Radiometers Early In-orbit Performances
MICAP Early In-orbit SSS/SST/WS & Soil Moisture
Conclusion

## Slide 22: MICAP NRT Joint Retrieval of SSS/SST/WS
Mode 2 (L/C/K CAP)
Cost function
priori errors of SST and WS are taken as 2 K and 2 m/s
Mode 1 (L-Rad Only)
Cost function
SST and WS are constrained strictly to the background field
SSS: NMEFC Forecasts
Others: ECMWF Forecasts

## Slide 23: MICAP Joint Retrieval of SSS/SST/WS
Single Pass Joint Retrieval (One day Coverage)
Validation approach
SSS: Compare with ARGO array and HYCOM ESPC-D-V02:
SST: NOAA In situ SST Quality Monitor (iQuam) and CMC Group for High Resolution Sea Surface Temperature (GHRSST)；
WS: NDBC Tropical Atmosphere/Ocean (TAO) array and RSS Cross-Calibrated Multi-Platform (CCMP)

## Slide 24: MICAP Single-Pass SSS/SST/WS
SSS
SST
WS
Observations from 2025.02.13 to 2025.03.13

## Slide 25: MICAP 8-day Average SSS/SST/WS
Wenyu WANG, Zhenzhan WANG, etc

## Slide 26: MICAP Monthly Averaged Global Soil Moisture
Huizhen CUI, Tianjie ZHAO, etc
（Shi et al., 2008; Zhao et al., 2021）
Multi-channel Collaborative Algorithm, MCCA

## Slide 27: OUTLINE
MICAP Instrument Description
MICAP Instrument Status During Commissioning Phase
MICAP L/C/K Radiometers Early In-orbit Performances
MICAP Early In-orbit SSS/SST/WS & Soil Moisture
Conclusion

## Slide 28: Conclusion
New Instrument
New Data
New Sciences…