## Slide 1
Yunkai Xu1, Yunzhao Wu1,
Yong Zhang2, Ling Sun2, and Zhiwei Wang2
Lunar-Based Cross-Calibration of GF-4 Mid-Infrared Band
Establishing a Radiometric Link from FY-4B/AGRI
1. Purple Mountain Observatory (PMO), CAS
2. National Satellite Meteorological Center (NSMC), CMA
Email address: ykxu@pmo.ac.cn
2026/03/26
1
GSICS Annual Meeting 2026, Ottawa, Canada | IR Session, 26 March 2026

## Slide 2
Presentation Outline
Model Comparison & Temperature Analysis
4
Radiometric Cross-Calibration
3
Lunar Observation Mechanisms & Datasets
2
Introduction & Motivation
1
Conclusions
5
2
2026/03/26
GSICS Annual Meeting 2026, Ottawa, Canada | IR Session, 26 March 2026

## Slide 3
1.1 The Calibration Gap of GF-4
1、Introduction & Motivation
Target Payload: GF-4/IRS (3.5–4.1 μm) • Critical for high-temperature monitoring (e.g., forest fires).
Hardware Limitation • No onboard blackbody calibrator. • Preprocessing coefficients inevitably degrade in orbit.
Current Bottlenecks • Site-based calibration: Susceptible to atmospheric absorption. • Dynamic range limits: Natural targets (< 330 K) are too cold for MIR.
The Calibration Gap • The high-gain, short-exposure (4 ms) mode completely lacks an absolute calibration standard.
GF-4 IRS
3
2026/03/26
GSICS Annual Meeting 2026, Ottawa, Canada | IR Session, 26 March 2026

## Slide 4
1.2 Why the Moon & Why FY-4B/AGRI?
1、Introduction & Motivation
Why the Moon? (Transfer Benchmark) • Highly Stable: Atmosphere-free and radiometrically stable over geological timescales. • Breaks Dynamic Limits: Overcomes the temperature limit of natural Earth targets (< 330 K), crucial for MIR high-temperature calibration.
The "Sub-Pixel" Challenge (e.g., IASI) • IFOV (14.3 mrad) > Lunar angular diameter (≈ 9 mrad). • Introduces severe deep-space background noise.
Why FY-4B/AGRI? (Radiometric Reference) • Onboard Blackbody: Absolute radiometric calibration (Bias < 0.12 K). • High Resolution: ~21.5 km/pixel, easily capturing the full lunar disk. • Co-orbital (GEO): Highly consistent viewing geometries with GF-4. • Perfect Spectral Match: Band 7 (3.75 μm) perfectly overlaps GF-4 MIR & avoids daytime saturation.
Parameter | GF-4 IRS MIR | FY-4B AGRI MIR
Spectral Range (μm) | 3.5-4.1 | 3.4-4.0
Center Wavelength (μm) | 3.80 | 3.75
IFOV (μrad) | 11.249 | 56
Ground Spatial Resolution (m/pixel) | 400 | 2000
Lunar Spatial Resolution (km/pixel) | 4.4 | 21.5
Pixel Array Size | 1024×1024 | 8×1
Detector Type | Staring Area Array | Linear Array Scanning
4
2026/03/26
GSICS Annual Meeting 2026, Ottawa, Canada | IR Session, 26 March 2026

## Slide 5
1.3 Cross-calibration framework
1、Introduction & Motivation
Data & Preprocessing
GF-4/IRS
Raw Images (2018)
FY-4B/AGRI
L1 Images (2024)
Background Subtraction
& Disk Integration
Geometric Correction & Disk Extraction
Uncalibrated Mean DN
FY-4B Phase Curve Model
Component Decoupling & Spectral Matching
RELAB
Lunar Soil Spectra
SRF Convolution (B6 & MIR)
Thermal Irradiance
Reflected Irradiance
Synthesized GF-4 Reference Irradiance
Reflectance Extrapolation Model
(B6 to MIR)
Brightness Temperature Retrieval
Calibration & Validation
Linear Fit & Calibration Coefficients
Internal Check
(vs. Reference Benchmark)
External Validation
(vs. TPM)
M3-corrected ROLO Model
GF-4 Reference Radiance
Thermophysical Analysis & Validation
5
2026/03/26
GSICS Annual Meeting 2026, Ottawa, Canada | IR Session, 26 March 2026

## Slide 6
2.1 Lunar Observing by FY-4B/AGRI and GF-4/IRS
2、Lunar Observation Mechanisms & Datasets
The Mismatch Challenge
Core Dilemma: Observation disparities and a ~5x resolution gap invalidate traditional pixel-level registration.
Methodological Shift: Strictly necessitates a full-disk integrated approach for radiometric transfer.
Imaging Mode: Area Array Staring
Spatial Resolution: ~4.4 km/px (High)
Capture: Single Exposure (active attitude maneuver)
Advantage: No image stitching;
avoids geometric/radiometric distortions.
Imaging Mode: Linear Array Scanning
Spatial Resolution: ~21.5 km/px (Moderate)
Capture: Passive Observation (During full-disk Earth scan).
Drawback: Introduces inter-frame staggering; requires geometric registration.
Staring
Scanning
GF-4 / IRS - The Monitored Target
FY-4B / AGRI - The Radiometric Reference
6
2026/03/26
GSICS Annual Meeting 2026, Ottawa, Canada | IR Session, 26 March 2026
Notes: 公式左侧为Stefan-Boltzmann定律，𝜖为月表发射率，约等于0.95；𝜎=5.67×10^(−8) 𝑊⋅𝑚^(−2)⋅𝐾^(−4)。月表按温度的四次方向外辐射热量。公式右侧由外部输入热流，以及热传导项构成。

## Slide 7
2.2 Datasets and Preprocessing
2、Lunar Observation Mechanisms & Datasets
Strict Data Selection • Timeframe: 2024 full-disk scanning data. • Band Choice: B7 selected for wide quantization (avoids high-temp saturation). • Condition: Strictly unexposed images.
Key Preprocessing Steps • Absolute Calibration: Via onboard blackbody (15-min intervals). • Staggering Correction: Sub-pixel translation to eliminate inter-frame jagged edges. • Oversampling Correction: Anisotropic resampling to correct oversampling (~33% horizontal).
FY-4B/AGRI Raw data (DN)
Calibrated Radiance
Staggering Correction
Oversampling Correction
& Extraction
Diverse lunar phase coverage from the FY-4B/AGRI
FY-4B AGRI
Jagged Edges
7
2026/03/26
GSICS Annual Meeting 2026, Ottawa, Canada | IR Session, 26 March 2026

## Slide 8
3、Radiometric Cross-Calibration
3.1 Reference Construction & Spatial Matching
2026/03/20
Model Framework：
: Observation phase angle.
, , , , : Free parameters for empirical curve fitting.
Normalize: Standardizes multi-temporal 2024 AGRI observations to constant distances (1 AU, 384,400 km).
Model: Fits the normalized data to the MIR lunar phase curve model.
Radiometric Transfer (De-normalize): Calculates the FY-4B equivalent irradiance under the exact GF-4 observation geometries.
Data Normalization：
Standardizes 2024 multi-temporal AGRI observations by eliminating variations in Sun-Moon () and satellite-Moon ( distances.
Lunar phase curve model and fitting results based on normalized FY-4B/AGRI measurements.
8
2026/03/26
GSICS Annual Meeting 2026, Ottawa, Canada | IR Session, 26 March 2026

## Slide 9
b) Thermal Component:
Emissivity (): GF-4 (0.7785): Highland (83%) / Mare (17%) mix (Wu et al., 2021); FY-4B (0.7816): Inversely mapped via RELAB formula.
Radiometric Transfer Workflow:
3、Radiometric Cross-Calibration
3.2 Component Decoupling and Spectral Matching
a) Reflected Component:
Baseline: FY-4B B6 (VNIR) disk reflectance calculated via M3-corrected ROLO.
MIR Extrapolation: Linearly extrapolated to MIR using 189 RELAB samples (spectrally resampled).
Solar Irradiance : ASTM E-490 solar spectrum.
Reflected Solar Derivation
Thermal Emission Derivation
opposition effect
9
Notes: 这里的𝐿_𝑡ℎ𝑒𝑟𝑚=𝐿_(𝑡𝑜𝑡𝑎𝑙(𝐹𝑌4𝐵))−𝐿_𝑟𝑒𝑓是照度还是亮度？？？？？？
文字部分描述不恰当，核心方法没说清楚，为什么选B6？光谱外推是干嘛的

## Slide 10
3、Radiometric Cross-Calibration
3.3 Radiometric Component Contributions & Calibration
Date | Phase Angle (deg) | Reflected Irradiance (W/m²/µm) | Thermal Irradiance (W/m²/µm) | Reflected Component (%) | Thermal Component (%)
2018.03.02 | -0.95 | 5.60×10-5 | 2.78×10-4 | 16.7 % | 83.3 %
2018.07.25 | -30.09 | 2.26×10-5 | 1.65×10-4 | 12.0 % | 88.0 %
2018.07.28 | 3.88 | 3.71×10-5 | 2.30×10-4 | 13.9 % | 86.1 %
2018.07.30 | 26.92 | 2.29×10-5 | 1.82×10-4 | 11.2 % | 88.8 %
2018.08.04 | 89.04 | 4.64×10-6 | 3.62×10-5 | 11.4 % | 88.6 %
Absolute Radiometric Calibration
Synthesis: (Linear superposition of decoupled components).
Performance: Achieved exceptional linearity across a wide dynamic range, validating the integrated lunar disk as an ideal point source.
Precision:
MIR Component Contributions
Thermal Dominance: > 83%
Thermal emission dominates the MIR budget, consistently accounting for 83.3–88.8%.
Reflected Fluctuation: 11% - 17%
Reflected component peaks near full moon (16.7%) due to opposition effect and stabilizes at ~11% at large phase angles.
The Necessity of Decoupling (SRF Impact)
Due to SRF differences, GF-4 exhibits systematically ~8% lower reflected irradiance but ~10% higher thermal irradiance than FY-4B.
10
2026/03/26
GSICS Annual Meeting 2026, Ottawa, Canada | IR Session, 26 March 2026

## Slide 11
4.1 Comparison with Thermophysical Model Results
4、Model Comparison & Temperature Analysis
1. Baseline: Traditional TPM:
Wu et al. (2021): A 1D heat conduction model assuming a smooth lunar surface.
2. Key Findings from Spatial Profiles
High-Signal Regions (Sub-solar Maria):
  Our radiances (red) are significantly higher in H1/H2.
  Insight: Captures the "Thermal Beaming" effect driven by micro-scale roughness, which smooth TPMs ignore.
Low-Signal Regions (Limb/Terminator):
  Our radiances (red) are systematically lower than TPM.
  Insight: Corrects TPM's unrealistic positive offset at the zero-signal intercept (caused by lacking dark-target constraints).
3. Core Advantage: Superior Dynamic Range
Incorporates a wider range of phase angles (up to 89°).
Provides comprehensive radiometric constraints for both high- and low-temperature targets across the full dynamic range.
11

## Slide 12
(a)
(b)
4、Model Comparison & Temperature Analysis
Internal Consistency Check (a):
Aligns perfectly with the FY-4B reference curve across all phase angles.
External Validation (vs. Traditional TPM)
Overall Improvement: Median relative error reduced from 6.0% to 3.8%.
Breakthrough under Extreme Geometries (b):
  At a large phase angle (≈ 89.04°), the TPM produced a severe error of 64.8%.
  Our method corrected this error to -2.8%.
Root Cause of TPM's Failure
Unconstrained Intercept: Lacking low-signal constraints, TPM yields an unrealistic positive offset at zero-signal.
Systematic Bias: This intercept massively inflates the integrated radiance for dark lunar disks (at large phase angles).
4.1 Comparison with Thermophysical Model Results
12
2026/03/26
GSICS Annual Meeting 2026, Ottawa, Canada | IR Session, 26 March 2026

## Slide 13
4、Calibration Results & Model Comparison
Temperature Retrieval Workflow
Decoupling:
(Wu et al., 2021).
Inversion: Brightness temperature () derived via Planck's law using updated calibration coefficients.
Spatial Characteristics:
  Albedo Control: Peak temperatures are localized in low-albedo mare regions near the sub-solar point.
  Thermal Inertia: Evening-side temperatures higher than morning-side at equivalent solar incidence.
  Topographic Modulation: Sun-facing slopes of large craters and ridges exhibit significant thermal enhancement.
Quantitative Temperature Statistics
Key Drivers:
albedo, topography,
thermal inertia……
Daytime Maximums ()
  2018.07.25: ~385.6 K
  2018.07.28: ~388.2 K
  2018.07.30: ~387.3 K
4.2 Application to Lunar Surface Temperature
13
2026/03/26
GSICS Annual Meeting 2026, Ottawa, Canada | IR Session, 26 March 2026
Notes: Using our new calibration coefficients, we retrieved the high-resolution brightness temperature maps of the lunar surface.
The retrieval method follows the work of Wu et al. 2021: first, we subtracted the reflected component from the calibrated total irradiance to isolate the thermal signal. Then, we derived the brightness temperature (𝑇_𝐵) via Planck's law.
These high-resolution maps reveal two clear thermophysical signatures. First, you can see strong topographic modulation, where sun-facing slopes of craters are significantly hotter. Second, and more importantly, the hotspot—the point of maximum temperature—is spatially shifted toward the low-albedo Oceanus Procellarum. This visually confirms the 1.20-degree thermal lag we modeled earlier, which is induced by thermal inertia.

## Slide 14
4、Calibration Results & Model Comparison
4.3 Micro-Roughness Effects
Empirical Cosine Power Model:
Sub-solar Temperatures ():
  Maria (): Higher (lower albedo basalt).
  Highlands (): Lower (high-albedo anorthosite).
"Limb Brightening" & Physical Coupling
Global Fit: (vs. Lambertian ).
Observed Trend: Maria () exhibit stronger limb brightening than Highlands ().
Coupling Mechanism:
  Highlands: High albedo triggers a sharp emissivity decrease at large emission angles.
  The Offset: This emissivity drop partially counteracts the roughness-induced "thermal beaming" in highlands, whereas the darker maria exhibit more prominent limb brightening effects.
14
2018.07.28
2026/03/26
GSICS Annual Meeting 2026, Ottawa, Canada | IR Session, 26 March 2026

## Slide 15
5、Conclusions
High-Precision Calibration
  RMSE=
  Error reduction:
  64.8% -2.8% (at 89°).
Thermophysical Insights
  MIR Thermal Dominance (>83%).
  Micro-roughness & Limb Brightening revealed.
Key Achievements
Robust & Universal: Cross-calibration framework for all GEO MIR sensors.
TPM-Free: Bypasses complex modeling and high-uncertainty parameters (albedo, inertia, RMS slope).
Practical: Low-cost, routine, & ideal for high-temp (fire) detection.
Methodological Advantages
Thermophysical Inversion: Inverting lunar surface properties from full-disk observations.
MIR Characterization: Deep-diving into unique lunar radiation behaviors.
On-orbit Monitoring: Long-term degradation tracking for infrared payloads.
Future Directions
3
2
1
The Moon can be effectively utilized as an ideal, high-stability calibration benchmark for GEO MIR sensors, with our empirical paradigm offering a robust and universal solution.
15
2026/03/26
GSICS Annual Meeting 2026, Ottawa, Canada | IR Session, 26 March 2026
Notes: 1. Key Achievements
High-Precision Calibration: Achieved stable coefficients for GF-4's high-gain mode (𝑅^2=0.9984) and corrected extreme geometry errors from 64.8% (TPM) to -2.8%.
Thermophysical Insights: Quantified MIR therm al dominance (>83%) and revealed the coupling of micro-roughness and directional emissivity via limb brightening analysis.
2. Methodological Advantages
Broader Dynamic Range: Provides comprehensive radiometric constraints by incorporating a wider range of phase angles (up to 89°), effectively covering both high- and low-temperature targets.
Universal & Simplified Paradigm:
  Offers a universal cross-calibration framework for GEO MIR sensors.
  Crucially, it bypasses the need for complex thermophysical modeling, avoiding the high uncertainties associated with TPM input parameters (albedo, thermal inertia, etc.).
Cost-Effective & Practical: The method is low-cost, easy to implement, and enables a fast, routine on-orbit calibration workflow.
High-Temperature Target: The Moon serves as an ideal high-temperature reference (>380 K) for calibrating channels designed for fire detection.
3. Future Directions
Refining Thermophysical Models: Utilize the unique, full-disk GEO lunar observations to refine existing thermophysical models and quantitatively invert lunar surface properties.
Investigating MIR Thermal Properties: Explore the unique thermal radiation characteristics of the lunar surface in the MIR band using the comprehensive full-disk dataset.
Long-Term Degradation Monitoring: Leverage the Moon as a stable benchmark to monitor the long-term radiometric degradation of infrared channels on Earth observation satellites.

## Slide 16
Thank you for your attention
Yunkai Xu1, Yunzhao Wu1,
Yong Zhang2, Ling Sun2, and Zhiwei Wang2
1. Purple Mountain Observatory (PMO), CAS
2. National Satellite Meteorological Center (NSMC), CMA
Email address: ykxu@pmo.ac.cn