## Slide 1: Research on the Non-Uniformity Correction Method for FY-3F OMS-N
Mao Jinghua1, Wang Yongmei 1, Wang Qian2 , Hu Xiuqing2, Yan Huanhuan2,Wang Yapeng2, Xu Jian1 , Fan Meng3 , Yu Chao3, Wei Fei1
1 NSSC 2 NSMC 3 AIRCAS
March 25, 2026

## Slide 2: Outline
FY-3F OMS-Nadir instrument Review
On-orbit Performance and Analysis
On-orbit Performance
WLS Analysis
Data Processing
Level 2 Product Validation
  AOD and AAI
  NO₂ TVCD
  Cloud Fraction
  Conclusion

## Slide 3: FY-3F OMS-Nadir instrument Review
The launch date for FY-3F is end of 2023 with a 8 year design lifetime
The Earth system's observation capacity has been strengthened, enhancing detection of stratospheric and tropospheric components like ozone and sulfur dioxide.
The Ozone Monitoring Suite - Nadir (OMS-N) is the payload of the FY-3F mission

## Slide 4: FY-3F OMS-Nadir instrument Review
The OMS-N
UV-VIS nadir viewing pushbroom grating spectrometer
Spectral range : 250-320nm,310-495nm
Spectral resolution :0.5-0.6nm
FOV :112°
Spatial resolution(nadir):7×7km2
The science products
Total column: O3，NO2，SO2 ，HCHO,BrO,OCIO
O3 profile
Aerosol：optical depth，absorbing index

## Slide 5: Outline
FY-3F OMS-Nadir instrument Review
On-orbit Performance Analysis and Data Processing
On-orbit Performance
WLS Analysis
Data Processing
Level 2 Product Validation
  AOD and AAI
  NO₂ TVCD
  Cloud Fraction
  Conclusion

## Slide 6: On-orbit Performance
目 录
CONTENTS
CONTENTS
（Image source: Xu, Wang, Chen, et al., Science China Earth Sciences）
CMA/NSMC and NSSC/CAS
O3
（Image source ：NSMC）
2025/10/9
Since October 2023, OMS-N has been tracking the spatiotemporal changes of the Antarctic ozone hole for two straight years.
Building on the FY-3A, B, C/TOU heritage, the China Meteorological Administration (CMA) has once again secured operational capacity for annual ozone hole monitoring.

## Slide 7: On-orbit Performance
SO2
SO2 retrievals of OMS and TROPOMI over the Nyamuragira volcano on November 3, 8, and 15, 2024. The missing pixels are the gap between the two orbits, or the Nan values in TROPOMI COBRA data
OMS-N demonstrates high sensitivity in SO₂ monitoring for volcanic eruptions and anthropogenic source pollution.
(Image source:SO2 retrievals of OMS and TROPOMI over the Nyamuragira volcano on November 3, 8, and 15, 2024. The missing pixels are the gap between the two orbits, or the Nan values in TROPOMI COBRA data)

## Slide 8: On-orbit Performance
NO2
The global distribution results demonstrate that the three NO₂ datasets from OMS, TROPOMI, and GOME-2 exhibit good consistency, particularly over anthropogenic activity regions including East Asia, Western Europe, the Middle East, and central-southern Africa.
Compared with GOME-2, OMS has a higher spatial resolution, showing a significant advantage.
（Image source:Yu Chao, et al. Aerospace Information Research Institute, Chinese Academy of Sciences）CMA/NSMC, AIR/CAS, NSSC/CAS

## Slide 9: On-orbit Performance
UVAI
North American wildfire emission plume
Large-scale biomass burning emission plume from "slash-and-burn" agriculture in southern Africa
Asian dust plume
African dust plume
North American wildfire emission plume
Asian dust plume
African dust plume
OMS-N UVAI
TROPOMI UVAI
Large-scale biomass burning emission plume from "slash-and-burn" agriculture in southern Africa
As Sentinel-5P is an afternoon satellite with a large overpass time gap from FY-3F, plume position drift occurs.
OMS-N and TROPOMI successfully captured the plume conditions of different events.
（ Image source: Meng Fan , et al. Aerospace Information Research Institute, Chinese Academy of Sciences）CMA/NSMC, AIR/CAS, NSSC/CAS

## Slide 10: On-orbit Performance
AOD
OMS-N AOD
MODIS AOD
AOD Validation Results
OMS-N
TROPOMI
MODIS
True Color Image
Cross-validation shows OMS-N AOD has better consistency with MODIS AOD (industry benchmark) than TROPOMI AOD.
In highly polluted areas, its spatial distribution agrees well with MODIS.
Correlation coefficient R > 0.85 stably, and > 0.9 in some typical regions.

## Slide 11: Analysis
We have found that striping artifacts are widespread in the product, leading to degraded data quality, so we conduct stripe analysis during the L1 data preprocessing stage.
0.5
0
Striping artifacts are widespread in the product, and are more severe in high-value regions.

## Slide 12: Analysis
DN Analysis – On-orbit White Light Source
The positions of peaks and valleys vary over time.
The amplitudes of peaks and valleys fluctuate over time.
Same Lamp Activation – Taking 340 nm as an Example
2023.09.22
2024.07.22
20250316
2023.10.10
2024.09.23

## Slide 13: Data Processing
DN Matrix (Spectral × Spatial × Scan Line)
Dark Current Correction
DN Extraction Adapted for SMILE Effect
Spatial-Domain Adaptive Multi-Pass Filtering
Perform Radiometric Coefficient Conversion
Reconstruct 3D Level‑1 Matrix
Comparison Before and After WLS Correction
Comparison Before and After Correction for Earth Observation

## Slide 14: Outline
FY-3F OMS-Nadir instrument Review
On-orbit Performance Analysis and Data Processing
On-orbit Performance
WLS Analysis
Data Processing
Level 2 Product Validation
  AOD and AAI
  NO₂ TVCD
  Cloud Fraction
  Conclusion

## Slide 15: Level 2 Product Validation
340 nm & 380 nm wavelength pair algorithm – Most sensitive to striping artifacts
400–460 nm DOAS algorithm
460–490 nm spectral fitting algorithm
L2 Product Validation
AOD&AAI
NO2
CLOUD

## Slide 16: Level 2 Product Validation
Before Correction
After Correction
0.5
0
Fine striping artifacts are significantly improved
AOD
(a)Original L1
(a) L1 after PRNU correction

## Slide 17: Level 2 Product Validation
0
AOD
(a) Comparison of AOD Retrieved from PRNU-Corrected OMS-N L1 Data, MODIS/Terra AOD, and TROPOMI AOD on 2025-02-17
(b) Comparison of AOD Retrieved from PRNU-Corrected OMS-N L1 Data, MODIS/Terra AOD, and TROPOMI AOD on 2025-05-19
Comparison of FY3F/OMS AOD Retrieval Results with Other Satellite AOD Products (After Correction on 2025-02-17 and 2025-05-19)

## Slide 18: Level 2 Product Validation
AAI
Aerosol Index, OMS (340/380)，Background-Removed
L1_PRNU1
L1_OLD
(a)
(b)
PRNU矫正前后反演的AAI对比图
Comparison of Retrieved AAI Before（left） and After（right） PRNU Correction
Optimization of Fine Striping Artifacts

## Slide 19: Level 2 Product Validation
NO2
(a)
(b)
Comparison Map of Retrieved NO₂ Before (a) and After (b) PRNU Correction

## Slide 20: Level 2 Product Validation
CLOUD
L1_OLD
L1_PRNU1
Comparison Map of Retrieved Cloud Parameters Before (a) and After (b) PRNU Correction

## Slide 21: Outline
FY-3F OMS-Nadir instrument Review
On-orbit Performance Analysis and Data Processing
On-orbit Performance
WLS Analysis
Data Processing
Level 2 Product Validation
  AOD and AAI
  NO₂ TVCD
  Cloud Fraction
  Conclusion

## Slide 22: Conclusion
Summary
The existing PRNU correction algorithm has improved fine random striping, and although it cannot completely eliminate striping problems, it has significantly increased the authenticity and reliability of the observational data.
Future work
Validate the PRNU correction algorithm on a larger dataset to test its broader performance.
Develop on-orbit stray light correction for the ultraviolet (UV) band to enhance the UV data quality
Email:maojinghua@nssc.ac.cn

## Slide 23: Conclusion
Thank You