## Slide 1
Zhao minjie, Si fuqi, Zhou haijin, Wu kaili
2026.3.25
EMI Stripe Error Correction Method and Results

## Slide 2: EMI instrument
Sun-synchronous
Trace gases:NO2,SO2,O3
Monitoring the emissions, distribution, and transmission of global pollutants plays an important role in atmospheric monitoring and research.
One day coverage
EMI
Launch in 2021

## Slide 3: EMI instrument
Spectral range | UV1:240－315nm、UV2:311－403nm; VIS1:401－550nm、VIS2:545－710nm;
Spectral resolution | 0.3-0.5nm
telescopy swath IFOV | IFOV 114 degrees
CCD detectors | 1024×1024 pixels (UV1/2); 1252×576(spectral ×spatial) pixels (VIS1/2)
ground pixel size | 24km×13km
mass | 95kg
size | 50cm×36cm×65cm
orbit | Polar,sun-synchronous average altitude:705km orbit perriod:98 minutes 53 seconds
EMI
Four Offner imaging spectrometers
Three observation modes

## Slide 4: EMI Irradiance
Solar+diffusers
Solar spectral image
spectral
spatial
0.43 nm
0.40 nm
Polynomial fit
Wavelength accuracy 0.05 nm

## Slide 5: EMI Irradiance
Verification
Average deviation is less than 4%
EMI and TROPOMI

## Slide 6
EMI L1B data processing
EMI L1B data
Processing time for one orbit is about 20 minutes
EMI Radiance

## Slide 7
 | TROPOMI | EMI
orbit | 820Km（太阳同步） | 705Km（太阳同步）
FOV | 2600Km | 2600Km
ascending time | 13:30 | 13:30
orbit period | T=98.8min | T=98.925min
spectral range | BD1:267-299nm BD2:299-331nm BD3:304-400nm BD4:400-498nm BD5:661-724nm | UV1:240-315nm UV2:311-403nm VIS1:401-550nm VIS2:545-710nm
spectral resolution | 0.5nm | 0.3-0.5nm
Spatial resolution | 7km×7km | 48km×13km
TROPOMI
EMI
Cross comparison
Relative error less than 6%
EMI Radiance

## Slide 8
DOAS(Differential Optical Absorption Spectroscopy) method
Reflectance spectrum
Atmospheric radiance
Solar irradiance
Difference between radiance and irradiance
Inversion algorithm
Introduce inversion error

## Slide 9: Inversion algorithm
Stripes along the orbit
Systematic overestimation or underestimation
Parameter | Content | Trace gas
Fitting Interval (nm) |  | 405-465
Polynomial | Order 5 | √
absorption cross section | 293 K (Thalman and Volkamer, 2013)[15] | √
absorption cross section | 223 K, 243 K (Bogumil et al, 2003)[16] | √
absorption cross section | 220 K, 298 K (Vandaele et al, 1996)[17] | √
BrO absorption cross section | 223 K (Fleischmann et al, 2004)[18] | √
Ring absorption cross section | Calculated using QDOAS | √
Parameter | Content | Trace gas
Fitting Interval (nm) |  | 405-465
Polynomial | Order 5 | √
 | 293 K (Thalman and Volkamer, 2013)[15] | √
 | 223 K, 243 K (Bogumil et al, 2003)[16] | √
 | 220 K, 298 K (Vandaele et al, 1996)[17] | √
BrO absorption cross section | 223 K (Fleischmann et al, 2004)[18] | √
Ring absorption cross section | Calculated using QDOAS | √
DOAS fitting for retrieving the NO2

## Slide 10: Stripe Error Correction
1. Solar calibration angle is different
Azimuth | 330°—345°
Elevation angle | -6°—+6°
Quartz Volume Diffuser (QVD)
Non ideal Lambertian characteristics
Scattering surface roughness
Solar spectrum depends on
the incident angle
Calibration angle varies with season and calibration time

## Slide 11: Stripe Error Correction
2. Sunlight path and Earthlight path is different
Radiometric response is different
Spectral response function is different
Spectral differences in irradiance and radiance
Earth light
Primary mirror
secondary
mirror
slit
Solar
diffuser
Folding mirror

## Slide 12: Stripe Error Correction
Stripe Correction method

## Slide 13: Stripe Error Correction
2022/6
2022/7
2022/8
2022/9
2022/10
2022/11
2022/12
2023/1
2023/2
2023/3
2023/4
2023/5
Fraunhofer line throughout one year
Annual raw solar spectrum (measured once a month)
STEP 1: Average raw solar spectrum throughout one year

## Slide 14: Stripe Error Correction
STEP 1: Average raw solar spectrum throughout one year
Single spectrum
Average spectrum
Average spectrum-VIS channel
Average spectrum-UV channel
Improve signal-to-noise ratio(SNR)
Eliminate spectral differences caused by solar incidence angles
Eliminate speckle effects on the rough surface of the diffuser
Reduce the introduced spectral structure

## Slide 15: Stripe Error Correction
STEP 1: Average raw solar spectrum throughout one year
Average relative deviation is 0.3%.
Relative deviation varies with wavelength, high-frequency structure may introduce inversion errors

## Slide 16: Stripe Error Correction
STEP 2: Correct sunlight and earthlight path
Average
solar spectrum
Corrected
solar spectrum
Irradiance response
Radiance response
VIS channel
UV channel
Difference is about 2.1%

## Slide 17: Stripe Error Correction
STEP 2: Correct sunlight and earthlight path
Full-Field-of-View Solar Reference Spectrum
VIS channel
UV channel
spectral
spatial
Average difference before and after correction is 1.6%
NO2 inversion bands comparison

## Slide 18: Stripe Error Correction
NO₂ SCD retrieval results
Before stripe correction
After stripe correction
RMS± 6×1015 molec/cm2
RMS± 0.8×1015 molec/cm2
Corrected SCD - Uncorrected SCD
± 2×10¹⁵ molec/cm²

## Slide 19: Stripe Error Correction
Before
After
Stripe noise significantly reduced
Better spatial continuity
systematic bias significantly corrected

## Slide 20
Thanks for your attention！