## Slide 1: GSICS VIS/NIR discussion
March 26, 2026

## Slide 2: GSICS VIS/NIR group goals
There is no SITSAT hyperspectral VIS/NIR/SWIR sensor to directly inter-calibrate coincident sensor channel radiances
Use multiple calibration strategies to transfer the calibration of the recommended calibration sensor reference
  Lunar, Ray-matching, DCC, deserts, Dome-C, Rayleigh scattering, sunglint, each target with a specific response range and scene types needed for retrieval
  Each strategy can be a GSICS product
  Combine the various calibration coefficients based on the square of their uncertainties
Use scene and channel specific spectral band adjustment factors (SBAFs) to account for the spectral response difference when inter-calibrating two sensors
  This is accomplished by using apriori channel convolved hyper-spectral radiances over specific earth targets
  Is a challenge when atmospheric absorption and scattering significant
NOAA-20 VIIRS is the recommended on-orbit calibration reference
  Data is freely available and assessable
  With a well funded calibration team (NOAA, NASA) with published on board calibration uncertainties
  Preferable: multiple satellite imager copies of overlapping records
  Preferable: reprocessing of the L1b record to remove anomalies on the record
  Any intercalibration between two sensors can be a GSICS products
TSIS-1 is the recommended solar spectra
  A high-resolution modeled spectra anchored to the well-calibrated TSIS instrument

## Slide 3: Discussion Items
Monthly web meeting topics
  Agency Ray-Matching algorithm comparisons, summer
    JMA, KMA, EUMETSAT, ISRO, NOAA, NASA – all have presented ray-matched comparisons
  SBAF datasets
    DESIS, ENMAP, HOAC data access
    SBAF tool host to allow users to formulate scene and channel specific SBAFs designed for their application and update channel spectral response functions
    CLARREO has 0.5 TB of MODTRAN hyperspectral simulated radiances
  PICS algorithms
    How do we find algorithm commonality among agency strategies
    Involve the CEOS community
  Orbital drift period vicarious strategies
    Terra, Aqua, Metop lessons learned
  GEOring
  CLARREO CPF updates and other SITSAT programs, TRUTHS, HOAC
  DCC ATBD dedicated meetings – next slide

## Slide 4: ATBD development
SWIR Band DCC ATBD is being written by Rajendra Bhatt (NASA)
  Follow on web meeting
VIS/NIR band DCC ATBD
  Start with EUMETSAT ATBD
  GSICS DCC VIS/NIR products start with JMA
  Write a DCC paper with contributions from participating agencies

## Slide 5: GSICS dashboard
Target intercalibration with reference sensor gains
  Gains over time of specific instrument pairs
  Gains of DCC, PICS, lunar, ray-matching for the same instrument pairs
sensor | reference | approach
GOES-19 | NOAA-20 | lunar
Meteosat-12 | lunar | DCC
 |  | Ray-matching
sensor
GOES-19
Meteosat-12
reference
NOAA-20 VIIRS
OLCI-B
reference
Lunar---
DCC(n20)---
Ray-matching(N20)---
Pull down menu
Pull down menu
Plot
We had discussion whether the gains are corrections to the l1b gain
The corrections are a stability analysis
Relative or normalized radiance%

## Slide 6: VIS/NIR algorithm leads needed
• Desert - EUMETSAT
DCC- NASA
SBAF
Ray-matching - JMA