## Slide 1
PATMOS-x v7.0: Updated Satellite-Based Climate Cloud Records since 1980
(calibration of visible channels)
Jongjin Seo, Coda Phillips, Andrew Heidinger, and Michael Foster
2026 GSICS web meeting
jseo47@wisc.edu
Notes: Hello,
I’m Jongjin Seo from University of Wisconsin-Madison.
I’m so happy to share some information about PATMOS-x v7 which is the updated satellite-based climate cloud records since 1980.

## Slide 2
What is the PATMOS-x (Pathfinder Atmospheres Extended)?
Initiated by NOAA in collaboration with the CIMSS (Cooperative Institute for Meteorological Satellite Studies) at the University of Wisconsin-Madison.
Aims to produce consistent satellite-based CDRs (Climate Data Records) of calibrated radiometric observations, cloud properties, and surface products using the CLAVR-x (Clouds from AVHRR Extended) software.
PATMOS-x v6 retrieves cloud properties from only AVHRR/HIRS observations from NOAA-06 to NOAA-19 and the MetOp satellites since 1980, while PATMOS-x v7 extends the record by processing VIIRS/CrIS observations from the Soumi NPP, NOAA-20 and NOAA-21 satellites.
Widely used in many atmospheric studies; long-term changes in maritime clouds (Seo et al. 2025), Cloud controlling factor framework (Seethala et al. 2015), Microphysical cloud properties in marine boundary layer (Rausch et al. 2010), cloud-aerosol interactions (Zhao et al. 2013), and spatial dsitrubiton of water / ice path in comparison with climate models (Eliasson et al. 2011)
1 / 11

## Slide 3
2 / 11

## Slide 4
Calibration of AVHRR’s visible channel
The AVHRR lacks onboard visible calibration system. Calibration coefficients of the AVHRR reflectance channels change over time. The sensitivity of the AVHRR decreases with time for reasons not fully understood and not predictable.
Various inter-calibration methods employed to improve consistency throughout the PATMOS-x record.
(Heidinger et al. 2002, 2003, 2010, and 2022; Molling et al. 2010)
1 / 11
(Heidinger et al. 2003)
(Foster et al. 2023)
Equatorial local over pass

## Slide 5
Using MODIS to calibrate AVHRR reflectance channels (Heidinger et al. 2002)
Find SNOs (Simultaneous Nadir Overpasses) between AVHRR satellites and MODIS onboard on Terra and Aqua.
: When two polar-orbiting satellites pass over nearly the same location at nearly the same time.
An implicit assumption of this process is that the MODIS reflectance are perfectly calibrated.
: Runs the MODTRAN4 for SBAF and Atmospheric Adjustment.
Stable targets:
a) Libyan desert
b) Taklimakan desert
bright and dry desert surface but BRDF effects from sand/dunes
c) Dome C in Antarctica
d) Greenland
bright snow/ice surface and stable but a limited period.
1 / 11

## Slide 6
Using MODIS to calibrate AVHRR reflectance channels (Heidinger et al. 2002)
Derive calibration slope [a second-order (quadratic) polynomial regression]; S(t) = a + bt + ct2
where t is the time after launch and C is digital count measured by the AVHRR detector for a pixel from 0 to 1023. Co is dark-space count that are measured during the space views and d is the Earth-Sun distance in AU. is the cosine of solar zenith angle.
1 / 11
(Heidinger et al. 2010)
Calibration Slope:
S = Rreference / (CAVHRR- C0)

## Slide 7
Single-gain vs Dual-gain
Employed a dual-gain approach to increase the sensitivity to dark scenes
Single-gain (AVHRR 1 / 2; NOAA-06 to NOAA-14) and Dual-gain (AVHRR 3; NOAA-15 to NOAA-19 and MetOps)
For the dual-gain, gain switch occurs at the prescribed switch count (near 500).
1 / 11
(Heidinger et al. 2002)
NOAA-16 vs MODIS
We can convert dual-gain count (Cdg) to the equivalent single-gain count (C) using equations:
Where Bdg is dual-gain switch count, Bsg is single gain of the switch count, D is the dark count on the
original dual-gain scale, Cd is the corresponding dark count on the converted single-gain scale.
For the single-gain, we derive a single calibration slope.
For the dual-gain, we derive calibration slopes for the low-gain and high-gain separately.
Low gain
High gain

## Slide 8
Morning-orbit vs Afternoon-orbit satellites
Afternoon-orbit: NOAA-07, 09, 11, 14, 16, 18, and 19. MetOp satellites. Crossed at roughly 13:30-14:30 local time.
:Relatively straightforward to calibrate reflectance using MODIS (also other AVHRR satellites) over stable targets.
Morning-orbit: NOAA-06, 08, 10, 12, 15, and 17. Crossed at roughly 07:30/19:30 local time
: Their daytime observations frequently occurred at large solar zenith angles, with increase BRDF effects, atmospheric path length, and sensitivity to illumination geometry.
Has fewer opportunities for direct MODIS comparison, with SNO-based collocations occurring primarily at high latitudes.
Use SNOs with other well-calibrated AVHRR sensors (usually afternoon-orbit) to transfer calibration to morning-orbit satellites. (AVHRRmorningAVHRRafternoon SNOs Method)
1 / 11

## Slide 9
3 / 11
2023 Calibration
2026 Calibration
Red dashed line: 2023
Updated instrument file
Dashed Line: 2023 calibration, Solid Line: 2026 calibration

## Slide 10
3 / 11
Updated instrument file
Dashed Line: 2023 Cal.
Solid Line: 2026 Cal.
MetOp-B
MetOp-C
2026 Cal. – 2023 Cal.
MetOp-B
MetOp-C
Simulated reflectance using following equation:
with assumption of a solar zenith angle is 30o and d of 1 AU
on 25 December 2025 (for the time after launch).

## Slide 11
3 / 11
Deep Convective Clouds (Doelling et al. 2010, 2013, and 2025)
Criteria
Latitude: 20S to 20N, BT at 11.0 um < 205 K
VIS and IR pixel homogeneity within 3% and 2 K
Solar Zenith Angle < 80o, Viewing zenith angle < 40o, 10o < Relative Azimuth Angle < 170o

## Slide 12
3 / 11
Deep Convective Clouds (Doelling et al. 2010, 2013, and 2025)
Still has a solar zenith angle dependence.

## Slide 13
3 / 11
Deep Convective Clouds
2023 Calibration
2026 Calibration
2023 Calibration
2026 Calibration
MetOp-B, MetOp-C

## Slide 14
3 / 11
Deep Convective Clouds
Use reference geometric angles
Apply XGBoost Machine Learning Technique.
Train from all satellites and calculate reference reflectance at
specific geometric angle.
Correction to a reference geometric angle:
Reference Geometric Angles for Rref: Solar Zenith Angle = 30o,
Sensor Zenith Angle = 10o, and Relative Azimuth Angle = 30o

## Slide 15
3 / 11
Deep Convective Clouds
2023 Calibration
2026 Calibration
2023 Calibration
2026 Calibration
MetOp-B, MetOp-C

## Slide 16
3 / 11
Deep Convective Clouds
2023 Calibration
2026 Calibration
2023 Calibration
2026 Calibration
MetOp-B, MetOp-C

## Slide 17
Thanks!

## Slide 18
3 / 11
Deep Convective Clouds
2023 Calibration
2026 Calibration
Black: AQUA Modis

## Slide 19
3 / 11
Deep Convective Clouds
Mean Refl (AVHRR):
2023 Calibration: 92.6%
2026 Calibration: 92.9%
Mean Refl (MODIS): 85.1%
2023 Calibration
2026 Calibration

## Slide 20
3 / 11
Deep Convective Clouds
MAE (All AVHRR):
2023 Calibration 5.3%
2026 Calibration 5.2%
RMSE (All AVHRR):
2023 Calibration 7.1%
2026 Calibration 7.1%
MAE Refl (MODIS): 5.7%
RMSE Refl (MODIS): 7.9%
2023 Calibration
2026 Calibration

## Slide 21
DCOMP (Daytime Cloud Optical and Microphysical Properties) Algorithm
Optimal Estimation Method based on bi-spectral approach to retrieve Cloud Optical Depth and Effective Radius.
1 visible & 1 near-infrared channels (mode 1: 0.65 & 1.60 um, mode 2: 0.65 & 2.10 um, and mode 3: 0.65 & 3.75 um)
PATMOS-x v6 used different DCOMP modes across satellites depending on AVHRR channel availability:
Mode 1 is used for NOAA-16, NOAA-17, and the MetOp series, while Mode 3 is used for the other satellites.
PATMOS-x v7 adopts DCOMP Mode 3 consistently across all satellites.
Timeseries of global monthly mean cloud effective radius
Pv7
Pv6
8 / 11